## Slide 1
Xianfeng Yang, Ph.D. Candidate
Department of Civil & Environmental Engineering
University of Maryland, College Park
Integrating of Arterial Signal and Freeway Off-ramp Controls for Commuting Corridors
Department of Civil & Environmental Engineering
University of Maryland

## Slide 2: Outline
Department of Civil & Environmental Engineering
University of Maryland
1
Research Background & Literature Review
2
Primary Tasks & System Framework
3
Model Formulations
4
Conclusions and Future Research Directions

## Slide 3
Congestion at Off-ramp Interchanged Area
Bottleneck
Department of Civil & Environmental Engineering
University of Maryland

## Slide 4
Field Observations
(National Highway No. 1, Chupei, Taiwan)
Department of Civil & Environmental Engineering
University of Maryland

## Slide 5: Integrated Off-Ramp Controls
Freeway
Intersection Signal Control
Arterial
Off-Ramp Interchange
Department of Civil & Environmental Engineering
University of Maryland
Signal Coordination Control
Integrated Off-ramp Traffic Control
Off- Ramp Queue Spillover Prevention

## Slide 6
Literature Reviews
Existing Studies
Pre-timed Signal Optimization Models
Real-time Signal Control Models
Integrated Control Models
Department of Civil & Environmental Engineering
University of Maryland

## Slide 7
Literature Reviews
Pre-timed Signal Optimization Models
Signal optimization at isolated intersections
Delay Minimization Model | Mathematical Programming Model
Matson et al. (1955), Webster (1958), Miller (1963), Robertson, (1969), Allsop (1971, 1972, 1975, 1981), Tully (1976) and Burrow (1987), Chang and Lin (2000) | Silcock, (1997,) Wong et al., (2003), Lan (2004), Yang et al., (2014)
Department of Civil & Environmental Engineering
University of Maryland

## Slide 8
Department of Civil & Environmental Engineering
University of Maryland
Literature Reviews
Pre-timed Signal Optimization Models
Signal optimization at arterial level
Minimizing Total Traffic Delay | Maximizing Progression Efficiency
TRANSYT (Robertson, 1969); TRANSYT 7-F (Wallace et al., 1988); Simulation-based (Yun and Park ,2006, Stevanovic et al., 2007); CTM-based (Lo, 1999; Lo et al., 2001; and Lo and Chow 2004); Others (Aboudolas et al., 2010; Zhang and Yin 2010, Li, 2012, Liu and Chang, 2011) | Morgan and Litter (1964), Litter (1966), Little et al., (1981), Gartner et al. (1991), Chaudhary et al. (2002), Tian and Urbanik (2007), Li (2014)

## Slide 9
Literature Reviews
Real-time Signal Control Models
Actuated Signal Control | Adaptive Signal Control
System Introduction (Boillot et al. 1992; ITE, 1997) Min green time selection (Kell and Fullerton, 1998) Max green time selection (Lin, 1985; Courage et al., 1989; Orcutt , 1993; Kell and Fullerton, 1998; Courage , 2003; Zhang and Wang, 2011) | SCOOT (Hunt et al. 1982; Ian et al., 1998; Dennis et al., 1991; Bretherton et al., 2005) SCATS (Luke, 1984, Gross, 2000, Gao, 2011) OPAC (Gartner et al., 1979; Gartner, 1983; Gartner et al., 1995; Gartner et al., 2001) RHODES (Mirchandani et al., 1995, 2000, 2001, 2004)
Department of Civil & Environmental Engineering
University of Maryland

## Slide 10
Literature Reviews
Integrated Control Models
Integrated Corridor Control | Off-ramp Control
Integration of multiple strategies such as: traffic diversion on-ramp metering speed limit control signal timing controls (Cremer and Schoof , 1989; Zhang and Hobeika, 1997; Wu and Chang, 1999; Chang et al., 1993; Papageorgiou, 1995; Berg et al., 2001; Li, 2010; Haddad et al. , 2013) | Eliminating the lane changing maneuvers (Daganzo et al., 2002; Rudjanakanoknad, 2012; Di et al., 2013) Detouring the flows to other non-congested areas (Gunther et al., 2012; Spiliopoulou et al., 2013, 2014) Optimizing signal timing at neighboring intersections (Messer, 1998; Tian et al., 2002; Li et al., 2009; Lim et al., 2011; Yang et al., 2014)

## Slide 11
Findings of Literature
Signal controls at arterial level (pre-timed & real-time):
may fall short of providing efficiency control at the off-ramp interchanged area;
Integrated corridor control:
may not be able to find the optimal solution for system control variables;
Off-ramp control with restricting lane changing or detouring flows:
may not be applicable in practice;
Off-ramp control with signal optimization at neighboring intersections:
more practical but many critical issues remain to be solved!
Department of Civil & Environmental Engineering
University of Maryland

## Slide 12: Outline
Department of Civil & Environmental Engineering
University of Maryland
1
Research Background & Literature Review
2
Primary Tasks & System Framework
3
Model Formulations
3
Conclusions and Future Research Directions

## Slide 13
Critical Research Issues
I – How to facilitate traffic flows to reach their destinations?
V – How to deal with the uncertainty of vehicles’ arrivals using real-time control functions?
II – How to analyze the demand pattern at the interchanged area?
III – How to optimize the signal plans to prevent the off-ramp queue spillover?
I – How to facilitate traffic flows to reach their destinations?
II – How to analyze the demand pattern at the interchanged area?
III – How to optimize the signal plans to prevent the off-ramp queue spillover?
V – How to deal with the uncertainty of vehicles’ arrivals using real-time control functions?
Department of Civil & Environmental Engineering
University of Maryland

## Slide 14
Critical Research Issues
I – How to facilitate traffic flows to reach their destinations?
V – How to deal with the uncertainty of vehicles’ arrivals using real-time control functions?
II – How to analyze the demand pattern at the interchanged area?
III – How to optimize the signal plans to prevent the off-ramp queue spillover?
Department of Civil & Environmental Engineering
University of Maryland

## Slide 15
Critical Research Issues
I – How to facilitate traffic flows to reach their destinations?
V – How to deal with the uncertainty of vehicles’ arrivals using real-time control functions?
II – How to analyze the demand pattern at the interchanged area?
III – How to optimize the signal plans to prevent the off-ramp queue spillover?
Identify traffic flows’ origins and destinations
O-D Estimation Model
Identify Critical Path
Department of Civil & Environmental Engineering
University of Maryland

## Slide 16
Critical Research Issues
I – How to facilitate traffic flows to reach their destinations?
II – How to analyze the demand pattern at the interchanged area?
III – How to optimize the signal plans to prevent the off-ramp queue spillover?
Department of Civil & Environmental Engineering
University of Maryland
V – How to deal with the uncertainty of vehicles’ arrivals using real-time control functions?

## Slide 17
Critical Research Issues
I – How to facilitate traffic flows to reach their destinations?
V – How to deal with the uncertainty of vehicles’ arrivals using real-time control functions?
II – How to analyze the demand pattern at the interchanged area?
III – How to optimize the signal plans to prevent the off-ramp queue spillover?
Department of Civil & Environmental Engineering
University of Maryland

## Slide 18
System Framework
Traffic Detectors
Historical Traffic Data
OD Estimation Model
OD flow pattern
Critical Traffic Paths
Signal Optimization Model
Multi-path Progression Model
Pre-timed Signal Plan
Real-time signal Control
Department of Civil & Environmental Engineering
University of Maryland

## Slide 19: Outline
Department of Civil & Environmental Engineering
University of Maryland
1
Research Background & Literature Review
2
Primary Tasks & System Framework
3
Model Formulations
4
Conclusions and Future Research Directions

## Slide 20
Model Development
Traffic Detectors
Historical Traffic Data
OD Estimation Model
OD flow pattern
Critical Traffic Paths
Signal Optimization Model
Multi-path Progression Model
Pre-timed Signal Plan
Real-time signal Control
Department of Civil & Environmental Engineering
University of Maryland

## Slide 21
Origin-Destination Estimation
In the literature, the main purpose of most O-D estimation models is providing essential information for traffic assignment or network simulation.
However, designing of signal plan at the off-ramp interchanged area have also raised the need of using O-D estimation for identifying critical traffic paths.
O-D Estimation
Static
Dynamic
Underdetermined system
Department of Civil & Environmental Engineering
University of Maryland

## Slide 22
Origin-Destination Estimation
Based on the dynamic O-D estimation technique, this study proposed three models with different measurement inputs:
Model I: only the link count data are available;
Model II: turning volumes at each intersection are available;
Model III: both intersection turning flows and real-time queue information are obtainable for model estimation.
Department of Civil & Environmental Engineering
University of Maryland

## Slide 23
O-D Estimation: Model I
Only the link count data are available
Loop Detector
Radar Sensor
Department of Civil & Environmental Engineering
University of Maryland

## Slide 24
Department of Civil & Environmental Engineering
University of Maryland
O-D Estimation: Model I
O-D flows and link travel time
Flow conservations and diversions
Flow conservations and diversions

## Slide 25
Estimation Algorithm
The dynamic O-D variables are assumed to follow the random walk process between successive time intervals:
Department of Civil & Environmental Engineering
University of Maryland

## Slide 26
Compute the linearized transformation matrix H(k)
Estimation Algorithm
Department of Civil & Environmental Engineering
University of Maryland
Initialization
Compute the mean link travel time
Update the estimation with extended Kalman filter

## Slide 27
O-D Estimation: Model II
Turning volumes at each intersection are available
Lane-based Radar Sensor
Fisheye camera
Department of Civil & Environmental Engineering
University of Maryland

## Slide 28
O-D Estimation: Model II
Flow conservations and diversions
For approach 1 and 3:
Turning flows at intersection l
Flow conservations and diversions
For approach 2 and 4:
Department of Civil & Environmental Engineering
University of Maryland

## Slide 29
O-D Estimation: Model III
Both intersection turning flows and real-time queue information are obtainable for model estimation
L
T
R
Signal progression
T
T
Camera Sensors
Radar Sensors
Department of Civil & Environmental Engineering
University of Maryland

## Slide 30
Department of Civil & Environmental Engineering
University of Maryland
O-D Estimation: Model III
Queue Length Estimation

## Slide 31
O-D Estimation: Model III
Queue Length Estimation
For outbound direction:
For inbound direction:
Department of Civil & Environmental Engineering
University of Maryland

## Slide 32
Model Evaluation
Arterial Topology of the Study Site
Models | Model I |  |  | Model II |  |  | Model III |  | 
 | MAE | MAPE | RMSE | MAE | MAPE | RMSE | MAE | MAPE | RMSE
Link flows | 4.54 | 18.56% | 5.48 | 4.10 | 16.31% | 5.21 | 3.99 | 15.92% | 4.99
Turning flows | 4.02 | 42.39% | 5.54 | 2.75 | 18.27% | 4.07 | 2.70 | 17.46% | 3.92
OD flows | 1.885 | 42.02% | 3.075 | 1.473 | 33.20% | 2.512 | 1.251 | 28.11% | 1.979
Department of Civil & Environmental Engineering
University of Maryland

## Slide 33
Model Evaluation
Ground Truth |  | Model I |  | Model II |  | Model III | 
OD Pair | Total Flows | OD Pair | Total Flows | OD Pair | Total Flows | OD Pair | Total Flows
9→12 | 1390 | 9→12 | 1658 | 9→12 | 1372 | 9→12 | 1480
6→12 | 765 | 6→12 | 985 | 6→12 | 860 | 6→12 | 784
9→1 | 756 | 9→4 | 649 | 9→4 | 727 | 9→1 | 722
6→4 | 729 | 4→7 | 497 | 4→7 | 571 | 6→4 | 642
12→7 | 553 | 4→8 | 465 | 12→6 | 544 | 12→7 | 540
12→1 | 472 | 9→1 | 427 | 9→1 | 531 | 12→1 | 452
Department of Civil & Environmental Engineering
University of Maryland

## Slide 34
Pre-timed Signal Design
Department of Civil & Environmental Engineering
University of Maryland
Traffic Detectors
Historical Traffic Data
OD Estimation Model
OD flow pattern
Critical Traffic Paths
Signal Optimization Model
Multi-path Progression Model
Pre-timed Signal Plan
Real-time signal Control

## Slide 35
Pre-timed Signal Design
Signal Optimization Model
Multi-path Progression Model
Objective:
maximizing intersection capacity
Control Variables:
common cycle length, green split
Objective:
maximizing progression efficiency
Control Variables:
offsets; phase sequences
Department of Civil & Environmental Engineering
University of Maryland

## Slide 36
Signal Timing Optimization
Objective function: Maximization of Intersection capacity
Apply a multiplier μ to the demand pattern

## Slide 37
Signal Timing Optimization
Maximization of intersection capacities
Flow <= Link Capacity
Sum of green = cycle length
Off-ramp queue constraint:
Queue < Link Length
Min & Max cycle length
Min & Max green time
Department of Civil & Environmental Engineering
University of Maryland

## Slide 38
Pre-timed Signal Design
Signal Optimization Model
Multi-path Progression Model
Objective:
maximizing intersection capacity
Control Variables:
common cycle length, green split
Objective:
maximizing progression efficiency
Control Variables:
offsets; phase sequences
Department of Civil & Environmental Engineering
University of Maryland

## Slide 39: Review of Two-way Progression
Within the green band, vehicles can pass the intersections without any stops.
outbound
inbound
Department of Civil & Environmental Engineering
University of Maryland

## Slide 40: What is Multi-Path Progression?
Department of Civil & Environmental Engineering
University of Maryland

## Slide 41: Critical Issues in Multi-Path Progression
1
How to formulate the optimization model to accommodate multiple traffic paths?
3
How to effectively eliminate some paths so as to produce the maximal progression benefit?
2
How to concurrently optimize the phase sequences?
Department of Civil & Environmental Engineering
University of Maryland

## Slide 42: Model I
Control Objective:
Interference Constraints:
:Bandwidth of an inbound path
:Bandwidth of an outbound path
:weighting factors
:green time for an inbound path at intersection k
:green time for an outbound path at intersection k
:part of green time that is before the band for an inbound path at intersection
:part of green time that is after the band for an outbound path at intersection
Department of Civil & Environmental Engineering
University of Maryland

## Slide 43: Model I
Progression Constraints:
For inbound directions:
where, is the total red time path experienced before the start of green at intersection .
For outbound directions:
where, is the total red time path experienced after the green time at intersection .
Inbound
outbound
Department of Civil & Environmental Engineering
University of Maryland

## Slide 44: Model II
Model 2: To optimize the phase sequence in the multi-path progression model.
To facilitate the phase sequence optimization, a set of binary variables are defined as follows:
Department of Civil & Environmental Engineering
University of Maryland

## Slide 45: Model II
To ensure the feasibility of the generated phase sequence, a set of constraints are defined as follows:
(optional)Phase and m are in a sequential order
A phase is never before itself.
Either phase is before phase , or phase is before phase .
If phase is before phase and phase is before phase , phase must be before phase .
(optional)Phase must be before phase
Department of Civil & Environmental Engineering
University of Maryland

## Slide 46: Model II
The interference constraints must be re-written as follows:
A set of binary parameters are defined to represent the phasing design:
Department of Civil & Environmental Engineering
University of Maryland

## Slide 47: Model II
For inbound directions:
Similarly, the progression constraints are given as follows:
For outbound directions:
?
?
?
?
:portion of green time that is before the band for an inbound path at intersection
:portion of green time that is after the band for an inbound path at intersection
:travel time between intersection and
:travel time between intersection and
Department of Civil & Environmental Engineering
University of Maryland

## Slide 48: Model III
Progression competition between different critical paths
  In practice, the identified critical paths may compete for the progression band.
  Thus, it might be infeasible or ineffective to find a synchronization plan which can offer reasonable bandwidths for all the critical paths.
  Hence, it is essential to eliminate some infeasible paths when designing signal progression.
Department of Civil & Environmental Engineering
University of Maryland

## Slide 49: Model III
To deal with the progression conflicts between critical paths, another set of constraints are introduced as follows to the model:
For inbound directions:
It is similar for outbound directions.
Department of Civil & Environmental Engineering
University of Maryland

## Slide 50: Model Summary
Model II
Model I
Model III
Department of Civil & Environmental Engineering
University of Maryland

## Slide 51
Numerical Test
Bottleneck

## Slide 52
Numerical Test
Three models are compared:
Model 1: TRANSYT-7F optimization Model;
Model 2: Proposed signal optimization model with MAXBAND for progression design;
Model 3: Proposed model;
Model | Intersection | CL | Φ1 | Φ2 | Φ3 | Φ4 | offset
Model-1 | 1 | 160 | 91 | 69 | / | / | 152
 | 2 | 160 | 41 | 32 | 60 | 27 | 0
 | 3 | 160 | 75 | 35 | 50 | / | 115
 | 4 | 160 | 92 | 37 | 31 | / | 76
Model-2 | 1 | 155 | 108 | 47 | / | / | 55
 | 2 | 155 | 39 | 27 | 63 | 26 | 85
 | 3 | 155 | 48 | 50 | 57 | / | 40
 | 4 | 155 | 95 | 32 | 28 | / | 0
Model-3 | 1 | 155 | 108 | 47 | / | / | 35
 | 2 | 155 | 39 | 27 | 63 | 26 | 47
 | 3 | 155 | 48 | 50 | 57 | / | 0
 | 4 | 155 | 95 | 32 | 28 | / | 138
Department of Civil & Environmental Engineering
University of Maryland

## Slide 53
Numerical Test
MOEs | Model 1 TRANSYT 7-F | Model 2 MAXBAND | Model 3 Proposed
Average Delay | 54.3 secs | 55.4 secs | 47.6 secs
Average # of Stops | 0.972 | 1.047 | 0.884
Average Speed | 34.7 km/h | 31.3 km/h | 40.5 km/h
To evaluate the signal plans produced by different models, a simulation network is developed with VISSIM.
Also, the VISSIM network has been well-calibrated with field data.
Intersection No. | Approach |  |  | 
 | WB | NB | EB | SB
1 | 1% | 0.6% | 2% | N/A
2 | 0.9% | N/A | 2% | 0.2%
3 | 2% | 3% | 0.6% | 1%
Percentage difference between simulated and field volume data
Netowork performance under the control of different models
Department of Civil & Environmental Engineering
University of Maryland

## Slide 54
Numerical Test
The time-dependent travel time on freeway mainline
Department of Civil & Environmental Engineering
University of Maryland

## Slide 55
Traffic Detectors
Historical Traffic Data
OD Estimation Model
OD flow pattern
Critical Traffic Paths
Signal Optimization Model
Multi-path Progression Model
Pre-timed Signal Plan
Real-time signal Control
Real-Time Signal Control

## Slide 56: Real-Time Signal Control
Off-ramp Queue Estimation
Traffic Detection System
Potential Freeway Breakdown?
Arterial Adaptive Signal Control
Dynamic Off-ramp Priority Control
No
Yes

## Slide 57: Off-ramp Queue Estimation Model
Location of dual-zone detectors on the target off-ramp
Short Detection Zone: collect traffic flow information;
Long Detection Zone: identify the presence of queue

## Slide 58: Off-ramp Queue Estimation Model
This study proposed two models in response to different congestion levels at the off-ramp:
Model I: off-ramp queue can be cleared during the green phase;
Model II: off-ramp queue cannot be cleared during the green phase.

## Slide 59: Model I
At time ε:
At time goff:
At time c:
equals the number of vehicles passed the upstream detector during time period [ε – toff , ε]
plus # of arrivals and minus # of departures
plus # of arrivals

## Slide 60: Model II
Two additional scenarios might be encountered:
Scenario 1: residual queue cannot reach the downstream detector;
Scenario 2: residual queue can reach the downstream detector;

## Slide 61: Scenario 1
At time c:
equals the number of vehicles passed the upstream detector during time period [η – toff , c]

## Slide 62: Scenario 2
If the residual queues have exceeded the downstream detector, the queue length at the end of a cycle can be approximated with :
Last cycle queue
Total Arrivals
Total Departures

## Slide 63: Real-Time Signal Control
Off-ramp Queue Estimation
Traffic Detection System
Potential Freeway Breakdown?
Arterial Adaptive Signal Control
Dynamic Off-ramp Priority Control
No
Yes

## Slide 64: Arterial Adaptive Signal Control
Intersection Signal Timing Adjustment
Objective
Minimization of intersection Delays
Solution Algorithm
Gradient Search
Adaptive Signal Progression Design
Objective
Maximization of Progression Efficiency
Solution Algorithm
Dynamic Programming
Department of Civil & Environmental Engineering
University of Maryland

## Slide 65: Intersection Signal Timing Adjustment
Step 1: Intersection Signal Timings Adjustment
Minimization of intersection total delay
Total delay estimation with queue
Arrival rate calculation
Departure rate estimation
Queue Estimation
Common cycle length constraint
Min & Max green time constraint
Max green time adjustment constraint

## Slide 66: Solution Algorithm
Gradient Search Algorithm:
Step 0: compute the intersection total delay if no green time adjustment is applied;
Step 1: for each phase p; find the adjustment direction (increase or reduce green time) based on the intersection total delay;
Step 1.1: increase the green time of phase p by 1 second and reduce the green time of another phase (the one can produce the minimal delay) by 1 second;
Step 1.2: decrease the green time of phase p by 1 second and increase the green time of another phase (the one can produce the minimal delay) by 1 second;
Step 1.3: compare the obtained delay from Step 1.1 &1.2 with the one from Step 0; find the green time adjustment direction;
Step 2: keep increasing or decreasing green time for phase p until no delay improvement is found or the green time constraint is violated.

## Slide 67: Adaptive Signal Progression Control
Green band of an outbound path between two intersections
Green band of an inbound path between two intersections

## Slide 68: Adaptive Signal Progression Control
Maximization of total green bandwidths
Estimation of green bandwidth for an outbound path
Estimation of green bandwidth for an inbound path
Identification of start of green for path i
Identification of end of green for path i
Max allowed offset adjustment constraint

## Slide 69: Solution Algorithm
Dynamic Programming:

## Slide 70: Solution Algorithm
Dynamic Programming:
Intersection 2
Intersection j
Intersection n
…
…
Intersection 1

## Slide 71: Real-Time Signal Control
Off-ramp Queue Estimation
Traffic Detection System
Potential Freeway Breakdown?
Arterial Adaptive Signal Control
Dynamic Off-ramp Priority Control
No
Yes

## Slide 72: Dynamic Off-ramp Priority Control
Intersection Signal Timing Adjustment
Objective
Minimization of intersection Delays
Solution Algorithm
gradient search
Adaptive Signal Progression Design
Objective
Maximization of Coordination Efficiency
Solution Algorithm
Dynamic programming

## Slide 73: Control Logic
Data Collection
Data
Analysis
Priority Control
Breakdown!
increasing the green time for the off-ramp flows;
providing signal progression priority to those path-flows from the target off-ramp.

## Slide 74: Intersection Signal Timing Adjustment with Off-ramp Priority
Step 1: computation of the minimum green extension to off-ramp flows
The minimal green extension will ensure the prevention of queue spillover until the end of the following signal cycle.

## Slide 75: Intersection Signal Timing Adjustment with Off-ramp Priority
Step 2: adaptive signal control with off-ramp priority
Green extension constraint

## Slide 76: Adaptive Signal Progression Control with Off-ramp Priority
Min bandwidth constraint for off-ramp path-flows

## Slide 77
Numerical Test

## Slide 78
Numerical Test
Queue Estimation Accuracy
Comparison of estimated and actual queue length at the off-ramp
The estimation errors of the off-ramp queue estimation model

## Slide 79
Numerical Test
Activation of off-ramp priority control function
Green extension time granted to the off-ramp flows

## Slide 80
Numerical Test
System Evaluation
The following three systems are tested for comparison:
Pre-timed Control System: using the proposed pre-timed models to generate the signal plans;
Adaptive Control System: only the proposed adaptive signal control model and dynamic signal progression model are implemented;
Proposed System: including the off-ramp queue estimation, arterial signal adaptive control, and off-ramp priority control.

## Slide 81
Numerical Test
The time-dependent travel time along the freeway mainline

## Slide 82
Numerical Test
Performance Index | Pre-timed System | Adaptive System | Proposed System
Ave number of stops | 2.391 | 1.711 (-28.4%) | 1.621 (-32.2%)
Ave speed (km/h) | 36.116 | 38.633 (+7.0%) | 39.25 (+8.7%)
Ave Network delay (s) | 89.065 | 73.77 (-13.7%) | 68.209 (-19.6%)
Network Performance

## Slide 83: Outline
Department of Civil & Environmental Engineering
University of Maryland
1
Research Background & Literature Review
2
Primary Tasks & Modeling Framework
3
System Framework & Model Formulations
4
Conclusions and Future Research Directions

## Slide 84
Conclusions
Summary of Contributions:
Developed an effective operational framework for the integrated traffic control at the off-ramp interchanged area;
Constructed a new O-D estimation model with real-time queue information;
Formulated a signal optimization model to prevent the off-ramp queue spillover;
Proposed a multi-path progression model to facilitate traffic flows to reach their destinations;
Advanced all key control models for real-time operations, in response to traffic fluctuations in practice.
Department of Civil & Environmental Engineering
University of Maryland

## Slide 85
Conclusions
Future Research Directions:
Development of an optimal traffic control model to concurrently account for the delay of traffic flows on the freeway and local arterial;
Integration of both on-ramp and off-ramp control strategies (ramp metering, variable speed limit, off-ramp priority, local signal adaptive control) for a large-scale corridor traffic management;
Enhancement of the current real-time signal control system with advanced information/communication technologies (e.g., connected vehicles).
Department of Civil & Environmental Engineering
University of Maryland

## Slide 86
THANKS & Questions?
Department of Civil & Environmental Engineering
University of Maryland