## Slide 1: Effect of short left-turn bay on intersection capacity
Yukai Huang

## Slide 2: Outline
Introduction
Objective
Literature review
Numerical Example
Deficiencies of the current studies
Further analysis

## Slide 3: Introduction
At intersections with high left-turn demand in conjunction with high opposing through flow, a protected left-turn signal phase, which can be provided before (leading) or after (lagging) the through movement, is generally used.
During the peak hour when there is a high demand of through and left-turn traffic, the length of the left-turn bay may affect the left-turn capacity and sometimes even the adjacent through capacity due to the occurrence of spillback and blockage situation.
  Blockage: during the green phase of left-turn traffic, the left-turn bay is blocked by the queue of through traffic.
  Spillback: during the green phase of the through traffic, the adjacent lane next to the left-turn bay is blocked by the queue of left-turn traffic.

## Slide 4: Objective
Objective:
  Analyze how the short left-turn bay will affect the intersection capacity under the condition that the left-turn is protected and leading.
Input:
  Arrival rate
  Geometric information (Number of lanes…)
  Length of left-turn bay
  Signal information (Cycle length…)

## Slide 5: Literature review
Year
Zong Z. Tian and Ning Wu (2006) JTE
Zhang and Tong (2008) TRB
Right-turn -> left-turn
Yin, Zhang and Wang (2010) TRB
Residual queue
Yin, Zhang and Wang (2011) TRB
Delay
Osei-Asamoah et al. (2010) TRB
Signal timing
Analytical model based
Simulation based
Haddad and Geroliminis (2012) STRC
Phase sequence
Reynolds and Zhou (2010) TRB
Reynolds and Zhou (2011) TRB
Messer and Fambro (1977) TRB
. . .
Related topic
Determent the length of left-turn bay
Next
Qi and Yu et al. (2007) TRB
Kikuchi et al. (2007) TRB
HCM (2010)

## Slide 6: Literature review
Zong Z. Tian and Ning Wu. Probabilistic Model for Signalized Intersection Capacity with a Short Right-Turn Lane, Journal of Transportation Engineering. 2006.
Pr(x=Vtotal) ~ Poisson Distribution
Pr(x=VRT) ~
Pt –> through vehicle
(1-pt) --> right turn vehicle
Back

## Slide 7: Literature review
Zhang and Tong. Modeling Left-Turn Blockage and Capacity at Signalized Intersection with Short Left-Turn Bay, TRB, 2008.
Back

## Slide 8: Literature review
Analytical model-based
Kai Yin, Yunlong Zhang, and Bruce X. Wang. Analytical Models for Protected plus Permitted Left-Turn Capacity at Signalized Intersection with Heavy Traffic, TRB, 2010.
  This paper adjusted Zhang and Tong’s paper (2008) by consider the residual queue of the through traffic under heavy traffic situation.
Kai Yin, Yunlong Zhang, and Bruce X. Wang. Modeling Delay During Heavy Traffic for Signalized Intersections with Short Left-Turn Bays, TRB, 2011.
  This paper used the same approach to further analyze the delay by considering blockage and spillback situations.
Abigail Osei-Asamoah, Ashish Kulshrestha, et al. Impact of Left-Turn Spillover on Through Movement Discharge at Signalized Intersections, TRB, 2010.
  This paper stated that Zhang and Tong’s paper (2008) is the only study identified that explicitly examined the impact of left-turn lane spillover on through movement discharge.
  This paper adjusted the probability of spillback situation by considering the arrival vehicles during red interval.
Jack Haddad, Nikolas Geroliminis. Capacity of arterials with left-turn queue spillbacks, STRC, 2012.
  This paper considered two different signal phase sequences.
Back

## Slide 9: Literature review
Simulation-based
William L. Reynolds, Xuesong Zhou, et al. Estimating Sustained Service Rates at Signalized Intersections with Short Left-Turn Pockets, TRB, 2010.
William L. Reynolds et al. Turn Pocket Blockage and Spillback Models, TRB, 2011
  Using cell transmission model with the assumption that the arrival pattern is uniformed.
Simulation-based method can consider more details and the result may be closer to reality, however it’s hard to be applied in general and it needs lots of energy and time.
Back

## Slide 10: Literature review
Determent the length of left-turn bay
  Yi Qi, Lei Yu, Mehdi Azimi, and Lei Guo. Determination of storage lengths of left turn lanes at signalized intersections. TRB, 2007.
    Estimate the queue length under 95% confident interval based on arrival pattern, and make the length of left-turn bay larger than it to avoid blockage situation.
  Shinya Kikuchi, Nopadon Kronprasert, and Masanobu Kii. Lengths of Turn Lanes on Intersection Approaches. TRB, 2007.
    Define some acceptable conditions (threshold probability) and calculate the suitable bay length that satisfies the thresholds.
Back

## Slide 11: Literature review
HCM 2010
  Capacity of unsignalized intersections with left-turn bays

## Slide 12: Literature review
HCM 2010
  Capacity of signalized intersections with left-turn bays
    No recommended model, only some simulation results under some assumed scenarios.
    For case‐specific applications, parameters that could influence the evaluation of bay overflow include the following:
      Number of lanes for each movement,
      Demand volumes for each movement,
      Impedance of left‐turning vehicles by oncoming traffic during permitted periods,
      Signal timing plan (cycle length and phase times),
      Factors that affect the number of left‐turn sneakers for left‐turn movements that have permitted operation, and
      Other factors that influence the saturation flow rates.
Back

## Slide 13: Numerical Example (Method from Zhang and Tong 2008)
Input:
  -Left-turn traffic arrival rate: λLT=400veh/h;
  -Through traffic arrival rate: λTH=800veh/h;
  -Number of through lanes: nl=2;
  -Length of left-turn bay: N=6veh;
  -Cycle length: C=90s;
  -Through traffic green time: gTH=27s;
  -Left-turn traffic green time: gLT=27s;
  -Saturation flow rate: s=2000veh/h;
  -Phase sequence: left-turn leading.

## Slide 14: Numerical Example (Method from Zhang and Tong 2008)
Step 1: Calculate the blockage probability:
  When number of arriving vehicle per cycle is less than 2N:
      Where,
      V is the total arriving vehicle number;
      vLT is the number of left-turn vehicles that can enter the left-turn bay before blockage;
      P(x=V) is the probability that arriving vehicle number equals to V under Poisson distribution
      with λ=λLT+λTH , which can be calculated as: ;
      pt is the percentage of through traffic, which equals to pt = λTH/(λLT+λTH);
  When number of arriving vehicle per cycle is less than 2N:
      Where,
      VMax is the maximum number of vehicle that possibly can arrival in one cycle;

## Slide 15: Numerical Example
Step 1: Calculate the blockage probability:
  Calculate the total probability of blockage:
  In this case, PBlockage=49.7%.

## Slide 16: Numerical Example
Step 2: Calculate the expected number of left-turn vehicles that can can arrive before blockage situation :
  When number of arriving vehicle per cycle is less than 2N:
      Where,
      V is the total arriving vehicle number;
      vLT is the number of left-turn vehicles that can arrive before blockage situation;
      P(x=V) is the probability that arriving vehicle number equals to V under Poisson distribution
      with λ=λLT+λTH , which can be calculated as: ;
      pt is the percentage of through traffic, which equals to pt = λTH/(λLT+λTH);
  When number of arriving vehicle per cycle is less than 2N:
      Where,
      VMax is the maximum number of vehicle that possibly can arrival in one cycle;

## Slide 17: Numerical Example
Step 2: Calculate the expected number of left-turn vehicles that can arrive before blockage situation:
  Calculate the total expected number:
  In this case, E(vLT)=2.06.
Step 3: Calculate the left-turn capacity under the given condition:
  Left-turn capacity:
  In this case, CLT=9.59 (veh/cycle) or 1280 (veh/h)

## Slide 18: Numerical Example
Step 4: Calculate the spillback probability:
  When number of arriving vehicle per cycle is less than 2N:
      Where,
      V is the total arriving vehicle number;
      vTH is the number of left-turn vehicles that pass adjacent through lane before spillback;
      P(x=V) is the probability that arriving vehicle number equals to V under Poisson distribution
      with λ=λLT+λTH , which can be calculated as: ;
      pt is the percentage of through traffic, which equals to pt = λTH/(λLT+λTH);
  When number of arriving vehicle per cycle is less than 2N:
      Where,
      VMax is the maximum number of vehicle that possibly can arrival in one cycle;

## Slide 19: Numerical Example
Step 4: Calculate the blockage probability:
  Calculate the total probability of blockage:
  In this case, PBlockage=27.5%.
Step 5: Calculate the expected number of through vehicles that can arrive before spillback in each cycle:
  Using the same method as step 3,
  So in this case, E(vTH)=0.95.
Step 6: Calculate the through capacity under the given condition:
  Through capacity:
  In this case, CTH=26.83 (veh/cycle) or 3577 (veh/h)
  So in summary, CLT=1280(veh/h), CTH=3577(veh/h).

## Slide 20: Deficiencies of the current studies
Process of a cycle:
LT:
TH:
Blockage
Blockage
Spillback
A
B
C
D(A’)

## Slide 21: Deficiencies of the current studies
Deficiency 1:
  The model has not considered that red phase for left-turn traffic starts earlier than the red phase for through traffic.
      Pr(Blockage)=Pr(XTH>=N+2)*Pr(XLT<=N+2)
  The initial queue for the left-turn traffic has been ignored.
      Pr(Blockage)=Pr(XTH>=N+2)*Pr(XLT<=N+2-qLT)

## Slide 22: Deficiencies of the current studies
Process of a cycle:
LT:
TH:
Blockage
Blockage
Spillback
A
B
C
Spillback?
D(A’)

## Slide 23: Deficiencies of the current studies
Video:

## Slide 24: Deficiencies of the current studies
Deficiency 2:
  The current model cannot well reflect the real spillback cases.
      Pr(Spillback)=Pr(XTH<=N+2)*Pr(XLT>=N+2)
  The probability of spillback situation may be overestimated.

## Slide 25: Deficiencies of the current studies
Process of a cycle:
LT:
TH:
Blockage
Blockage
Spillback
A
B
C
Spillback?
D(A’)

## Slide 26: Further analysis
Idea
  Point A:
  Existing queue (qLT)
  Point A  Point C:
  Probability of blockage (Prblock)
  Expected # of LT vehicles that pass the intersection (Vcapacity)
  Expected # of LT vehicles that do not pass (Vnopass)
  Point C  Point A’:
  Probability of spillback under all different cases (Prspill)
  New expected existing queue for next cycle (qLT’)
LT:
TH:
A
B
C
D(A’)

## Slide 27: Further analysis
Input:
  Left-turn traffic arrival rate: aLT (veh/h);
  Total through traffic arrival rate: aTH (veh/h);
  Cycle length: C (s);
  Green time for through traffic: gTH (s);
  Green time for left-turn traffic: gLT (s);
  Bay length: L (veh);
  Saturation flow rate: s (veh/h);
  Initial existing left-turn queue at A:
LT:
TH:
A
B
C
D(A’)

## Slide 28: Further analysis
Notation:
  i is the number of through vehicles arriving during AC;
  j is the number of left-turn vehicles arriving during AC;
  k is the number of left-turn vehicles arriving the intersection before the Lth through arriving vehicles;
  Cij is the expected number of left-turn vehicles that can pass the intersection by the end of green interval of left-turn phase, under the given i and j;
  Rij is the expected number of left-turn vehicles that stay in queue at the end of green interval of left-turn phase, under the given i and j;
  sTH is the maximum number of vehicles that can pass the intersection during the green interval for through traffic in one cycle;
  sLT is the maximum number of vehicles that can pass the intersection during the green interval for left-turn traffic in one cycle;
  CTH and CLT are the capacity for through and left-turn traffic.
LT:
TH:
A
B
C
D(A’)
Lth

## Slide 29: Further analysis
Assumptions:
  Arrival patterns of through and left-turn traffic follow two stable and independent Poisson distributions respectively;
  Traffic demand is under saturation condition;
  All left-turn vehicles use the left-side through lane before reaching the left-turn bay;
  Signal timing is fixed.
LT:
TH:
A
B
C
D(A’)

## Slide 30: Further analysis
Starting Point: A
  Assume is given, and
Point A -> Point C (Blockage condition)
  Case 1
  When i<L
  (Through arriving vehicles is less than the bay length, no blockage)
  Prblock=0%
  and ;
  and .
LT:
TH:
A
B
C
D(A’)

## Slide 31: Further analysis
Point A -> Point C
  Case 2
  When i L and j<
  (All left-turn vehicles arrive before Lth through vehicle will be discharged during the green interval BC, and blockage always happens)
  Prblock=100%
  P(k)= (The probability that k left-turn vehicles arrive before Lth through vehicle)
  E(k)= (The expected value of k under blockage condition)
  and
  and
LT:
TH:
A
B
C
D(A’)
Lth

## Slide 32: Further analysis
Point A -> Point C
  Case 3
  When i L and j
  (When the number of left-turn vehicles arrive before Lth through vehicle exceed the maximum discharging vehicle number, then no blockage)
    Case 3.A (Blockage)
    When k<
    Prblock=100%
    P(k)= (The probability that k left-turn vehicles arrive before Lth through vehicle)
    Eblock(k)= (The expected value of k under blockage condition)
LT:
TH:
A
B
C
D(A’)

## Slide 33: Further analysis
Point A -> Point C
  Case 3
  When i L and j
  (When the number of left-turn vehicles arrive before Lth through vehicle exceed the maximum discharging vehicle number, then no blockage)
    Case 3.B (No Blockage)
    When k
    Prblock=0%
    P(k)= (The probability that k left-turn vehicles arrive before Lth through vehicle)
    ENoblock(k)= (The expected value of k under no blockage condition)
LT:
TH:
A
B
C
D(A’)

## Slide 34: Further analysis
Point A -> Point C
  Case 3
  So the final E(k)=Eblock(k)+ENoblock(k)
  and
  and
  Here all cases during AC are discussed.
So the expected capacity of left-turn traffic can be calculated:
=
  Where P(i) ~ Poisson (λ is unknown)
  P(j) ~ Poisson (λ=)
LT:
TH:
A
B
C
D(A’)

## Slide 35: Further analysis
Point C -> Point D (Spillback condition)
  Since the Rij is obtained at Point C, so the spillback probability can be calculated as:
  Case 1:
  When
  (spillback)=1 (Already spillback)
  Case 2:
  When
  (spillback)=P(x>=L+1-)
    Where P(x) ~ Poisson (λ=)
LT:
TH:
A
B
C
D(A’)

## Slide 36: Further analysis
So the final probability of spillback can be calculated:
=
  Where P(i) ~ Poisson (λ=)
  P(j) ~ Poisson (λ=)
So the final capacity of through traffic can be calculated:
=（1-）** +
  Where nl is the number of through lanes
So the new formed existing queue at D can be calculated:
+
  This new existing queue can be used into the next iteration.
LT:
TH:
A
B
C
D(A’)

## Slide 37: Further analysis
Problem 1:
  Arrival rate of through traffic in adjacent through lane is unknown.
=
  Where P(i) ~ Poisson (λ is unknown)
  P(j) ~ Poisson (λ=)
Method:
  Build a model to estimate the arrival rate of through traffic in adjacent through lane, based on the left-turn volume, total through volume and length of left-turn bay.

## Slide 38: Further analysis
Input:
  Left-turn arrival rate: VLT (veh/h)
  Total through arrival rate: VTH (veh/h)
  Left-turn bay length: L (veh)
Assumption:
  All left-turn traffic use the adjacent though lane before entering the left-turn bay.
Output:
  Arrival rate of through traffic at adjacent through lane: V1 (veh/h)

## Slide 39: Further analysis
Method:
  Case 1: L=0 (No left-turn bay)
    All traffic evenly distribute between two through lanes:
    V1+VLT=VTH-V1 -> V1=VTH/2-VLT/2
  Case 2: L-> (Exclusive left-turn lane)
    All through traffic evenly distribute:
    V1=VTH/2
  Normal case: With the increase of L, the V1 increases
Length of left-turn bay
    VTH/2-VLT/2
    VTH/2
Assumed relation:

## Slide 40: Further analysis
Use simulation results to obtain the parameter a.
  Scenarios:
Chart: 
| 4 | 6 | 8 | 10
case 1 | 203 | 233 | 279 | 296
case 2 | 297 | 340 | 355 | 368
case 3 | 77 | 89 | 118 | 129
case 4 | 131 | 151 | 159 | 161
 | LT vph | TH vph | Bay length | # veh in Lane 1 | Parameter a
Case 1 | 400 | 800 | 4 | 203 | 0.00378
 | 400 | 800 | 6 | 233 | 0.03005
 | 400 | 800 | 8 | 279 | 0.06282
 | 400 | 800 | 10 | 296 | 0.06539
Case 2 | 200 | 800 | 4 | 297 | -0.00739
 | 200 | 800 | 6 | 340 | 0.08514
 | 200 | 800 | 8 | 355 | 0.09981
 | 200 | 800 | 10 | 368 | 0.11394
Case 3 | 400 | 400 | 4 | 77 | 0.12153
 | 400 | 400 | 6 | 89 | 0.09813
 | 400 | 400 | 8 | 118 | 0.11145
 | 400 | 400 | 10 | 129 | 0.10356
Case 4 | 200 | 400 | 4 | 131 | 0.09277
 | 200 | 400 | 6 | 151 | 0.11889
 | 200 | 400 | 8 | 159 | 0.11145
 | 200 | 400 | 10 | 161 | 0.09416
 |  |  |  | AVG | 0.08159
Model to estimate the V1 :

## Slide 41: Further analysis
Problem 2:
  Initial existing queue -> not known
Method:
  Given any reasonable queue at first and after several iterations, see if the queue will become stable.

## Slide 42: Further analysis
Result
  left-turn traffic arrival rate (veh/hour): 400vph
  through traffic arrival rate (veh/hour): 800vph
  the saturation flow rate (veh/hour) : 2000vph
  number of through lanes: 2
  cycle length AD: 90s
  through traffic green interval CD: 27s
  left-turn traffic green interval BC: 27s
  the length of left-turn lane : 6 veh
  Note: if the input changes, the output shows the same pattern as above.
Chart: 
Initial 12 | 12 | 7.0567 | 3.8024 | 3.3062 | 3.2578 | 3.2578
Initial 8 | 8 | 4.1769 | 3.3062 | 3.2578 | 3.2578 | 3.2578
Initial 4 | 4 | 3.3062 | 3.2578 | 3.2578 | 3.2578 | 3.2578
Initial 0 | 0 | 3.2167 | 3.2578 | 3.2578 | 3.2578 | 3.2578
Conclusion:
  Result shows that no matter the starting existing queue is, after several iteration, the left-turn queue and Point D becomes stable.
  When the existing queue becomes stable, the resulting left-turn and through capacity should be regarded as the capacity for the target approach.

## Slide 43: Model validation
Scenarios
  Intersection geometry:
    Target approach: Two through lanes, one left-turn bay.
    Other approaches: Two through lanes, one left-turn lane.
    Length of left-turn bay: 4veh, 6veh, 8veh, 10veh.
  Traffic volume:
    Target approach (W->E):
    Through traffic: 500vph, 600vph, 700vph, 800vph.
    Left-turn traffic: 200vph, 300vph.
    Saturation flow rate: 2000vph
    Opposite approach (E->W): The same with target approach.
    Other approaches (N->S & S->N): Keep the same with each other and change with W-E approaches in order to keep the CLV(1800vph) and cycle length(90s) constant.
      Reason: Input of the model is the arrival vehicles per cycle;
      When one variables (through or left-turn volume) stay the same, the green time stay the same.
  Signal plan:
    Cycle length: 90s (If using webster’s equation: 75s)
    Green splits: Using Synchro to obtain the optimal plans.
  Simulation:
    Using CORSIM to run for 3600 time steps.
    Every scenario uses three different random seeds to observe the number of blockage and spillback situation in order to get the average probability.
1200-Vth
600-VLT

## Slide 44
Scenarios | LT vph | TH vph | Bay length | # of TH lanes | CYCLE | TH GREEN | LT GREEN
Case 1 | 300 | 800 | 4 | 2 | 90 | 28 | 21
 | 300 | 800 | 6 | 2 | 90 | 28 | 21
 | 300 | 800 | 8 | 2 | 90 | 28 | 21
 | 300 | 800 | 10 | 2 | 90 | 28 | 21
Case 2 | 300 | 700 | 4 | 2 | 90 | 24 | 21
 | 300 | 700 | 6 | 2 | 90 | 24 | 21
 | 300 | 700 | 8 | 2 | 90 | 24 | 21
 | 300 | 700 | 10 | 2 | 90 | 24 | 21
Case 3 | 300 | 600 | 4 | 2 | 90 | 24 | 22
 | 300 | 600 | 6 | 2 | 90 | 24 | 22
 | 300 | 600 | 8 | 2 | 90 | 24 | 22
 | 300 | 600 | 10 | 2 | 90 | 24 | 22
Case 4 | 300 | 500 | 4 | 2 | 90 | 21 | 22
 | 300 | 500 | 6 | 2 | 90 | 21 | 22
 | 300 | 500 | 8 | 2 | 90 | 21 | 22
 | 300 | 500 | 10 | 2 | 90 | 21 | 22
Case 5 | 200 | 800 | 4 | 2 | 90 | 27 | 16
 | 200 | 800 | 6 | 2 | 90 | 27 | 16
 | 200 | 800 | 8 | 2 | 90 | 27 | 16
 | 200 | 800 | 10 | 2 | 90 | 27 | 16
Case 6 | 200 | 700 | 4 | 2 | 90 | 26 | 16
 | 200 | 700 | 6 | 2 | 90 | 26 | 16
 | 200 | 700 | 8 | 2 | 90 | 26 | 16
 | 200 | 700 | 10 | 2 | 90 | 26 | 16
Case 7 | 200 | 600 | 4 | 2 | 90 | 24 | 16
 | 200 | 600 | 6 | 2 | 90 | 24 | 16
 | 200 | 600 | 8 | 2 | 90 | 24 | 16
 | 200 | 600 | 10 | 2 | 90 | 24 | 16
Case 8 | 200 | 500 | 4 | 2 | 90 | 22 | 16
 | 200 | 500 | 6 | 2 | 90 | 22 | 16
 | 200 | 500 | 8 | 2 | 90 | 22 | 16
 | 200 | 500 | 10 | 2 | 90 | 22 | 16
Scenarios

## Slide 45
Results
LT vph | TH vph | Bay length | # of TH lanes | CYCLE | TH GREEN | LT GREEN | Blocakge Prob |  |  | Spillback Prob |  | 
 |  |  |  |  |  |  | Simulation | Proposed Model | Current model | Simulation | Proposed Model | Current model
300 | 800 | 4 | 2 | 90 | 28 | 21 | 73.33% | 71.20% | 65.27% | 35.83% | 42.70% | 34.67%
300 | 800 | 6 | 2 | 90 | 28 | 21 | 48.33% | 42.40% | 67.69% | 6.67% | 5.97% | 30.69%
300 | 800 | 8 | 2 | 90 | 28 | 21 | 23.33% | 19.10% | 63.92% | 0.83% | 0.00% | 24.53%
300 | 800 | 10 | 2 | 90 | 28 | 21 | 0.00% | 6.53% | 49.36% | 0.00% | 0.00% | 15.09%
300 | 700 | 4 | 2 | 90 | 24 | 21 | 55.00% | 62.85% | 58.28% | 25.83% | 32.01% | 41.57%
300 | 700 | 6 | 2 | 90 | 24 | 21 | 35.83% | 32.83% | 58.51% | 1.67% | 3.20% | 38.31%
300 | 700 | 8 | 2 | 90 | 24 | 21 | 10.83% | 12.69% | 51.07% | 0.00% | 0.02% | 30.36%
300 | 700 | 10 | 2 | 90 | 24 | 21 | 0.00% | 3.78% | 34.14% | 0.00% | 0.00% | 17.70%
300 | 600 | 4 | 2 | 90 | 24 | 22 | 48.33% | 45.80% | 49.83% | 11.67% | 21.74% | 49.83%
300 | 600 | 6 | 2 | 90 | 24 | 22 | 30.83% | 18.06% | 47.09% | 0.83% | 0.19% | 47.09%
300 | 600 | 8 | 2 | 90 | 24 | 22 | 7.50% | 5.36% | 36.24% | 0.00% | 0.00% | 36.24%
300 | 600 | 10 | 2 | 90 | 24 | 22 | 0.00% | 0.12% | 19.86% | 0.00% | 0.00% | 19.86%
300 | 500 | 4 | 2 | 90 | 21 | 22 | 32.50% | 28.12% | 39.80% | 8.33% | 12.50% | 59.43%
300 | 500 | 6 | 2 | 90 | 21 | 22 | 14.17% | 8.42% | 33.78% | 0.00% | 0.07% | 56.41%
300 | 500 | 8 | 2 | 90 | 21 | 22 | 0.83% | 1.80% | 21.43% | 0.00% | 0.00% | 41.38%
300 | 500 | 10 | 2 | 90 | 21 | 22 | 0.00% | 0.00% | 8.98% | 0.00% | 0.00% | 21.32%
200 | 800 | 4 | 2 | 90 | 27 | 16 | 67.50% | 81.31% | 82.47% | 13.33% | 19.58% | 17.26%
200 | 800 | 6 | 2 | 90 | 27 | 16 | 54.17% | 52.90% | 84.55% | 0.83% | 1.41% | 11.32%
200 | 800 | 8 | 2 | 90 | 27 | 16 | 20.00% | 26.38% | 75.05% | 0.00% | 0.00% | 5.87%
200 | 800 | 10 | 2 | 90 | 27 | 16 | 1.67% | 9.81% | 53.66% | 0.00% | 0.00% | 2.01%
200 | 700 | 4 | 2 | 90 | 26 | 16 | 57.50% | 71.39% | 77.24% | 10.83% | 15.37% | 22.09%
200 | 700 | 6 | 2 | 90 | 26 | 16 | 39.17% | 40.17% | 76.69% | 1.67% | 0.72% | 15.20%
200 | 700 | 8 | 2 | 90 | 26 | 16 | 15.83% | 16.29% | 61.69% | 0.00% | 0.00% | 7.64%
200 | 700 | 10 | 2 | 90 | 26 | 16 | 0.00% | 4.90% | 37.52% | 0.00% | 0.00% | 2.42%
200 | 600 | 4 | 2 | 90 | 24 | 16 | 41.67% | 58.63% | 70.01% | 8.33% | 10.97% | 28.42%
200 | 600 | 6 | 2 | 90 | 24 | 16 | 26.67% | 27.09% | 65.10% | 3.33% | 0.36% | 20.03%
200 | 600 | 8 | 2 | 90 | 24 | 16 | 5.83% | 8.79% | 45.03% | 0.00% | 0.00% | 9.50%
200 | 600 | 10 | 2 | 90 | 24 | 16 | 0.00% | 2.11% | 22.06% | 0.00% | 0.00% | 2.77%
200 | 500 | 4 | 2 | 90 | 22 | 16 | 27.50% | 42.62% | 59.99% | 5.00% | 6.05% | 36.56%
200 | 500 | 6 | 2 | 90 | 22 | 16 | 12.50% | 14.72% | 49.43% | 3.33% | 0.16% | 25.54%
200 | 500 | 8 | 2 | 90 | 22 | 16 | 5.00% | 3.57% | 27.37% | 0.00% | 0.00% | 11.20%
200 | 500 | 10 | 2 | 90 | 22 | 16 | 0.00% | 0.53% | 10.07% | 0.00% | 0.00% | 3.01%

## Slide 46
Results:
Case 1:
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.73333 | 0.48333 | 0.23333 | 0
Proposed M | 0.712 | 0.424 | 0.191 | 0.0653
Current M | 0.65274 | 0.67692 | 0.63918 | 0.49359
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.35833 | 0.066667 | 0.0083333 | 0
Proposed M | 0.427 | 0.0597 | 0 | 0
Current M | 0.34665 | 0.30688 | 0.24528 | 0.15087
Bay length
Case 2:
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.55 | 0.35833 | 0.10833 | 0
Proposed M | 0.6285 | 0.3283 | 0.1269 | 0.0378
Current M | 0.58281 | 0.58509 | 0.51071 | 0.34136
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.25833 | 0.016667 | 0 | 0
Proposed M | 0.3201 | 0.032 | 0.0002 | 0
Current M | 0.41569 | 0.38311 | 0.30358 | 0.17703

## Slide 47
Results:
Case 3:
Case 4:
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.48333 | 0.30833 | 0.075 | 0
Proposed M | 0.458 | 0.1806 | 0.0536 | 0.0012
Current M | 0.49825 | 0.47085 | 0.36238 | 0.1986
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.11667 | 0.0083333 | 0 | 0
Proposed M | 0.2174 | 0.0019 | 0 | 0
Current M | 0.49825 | 0.47085 | 0.36238 | 0.1986
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.325 | 0.14167 | 0.0083333 | 0
Proposed M | 0.2812 | 0.0842 | 0.018 | 0
Current M | 0.39803 | 0.33781 | 0.21425 | 0.089764
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.083333 | 0 | 0 | 0
Proposed M | 0.125 | 0.0007 | 0 | 0
Current M | 0.59426 | 0.56407 | 0.41383 | 0.21318

## Slide 48
Results:
Case 5:
Case 6:
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.675 | 0.54167 | 0.2 | 0.016667
Proposed M | 0.8131 | 0.529 | 0.2638 | 0.0981
Current M | 0.82471 | 0.8455 | 0.75045 | 0.53655
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.13333 | 0.0083333 | 0 | 0
Proposed M | 0.1958 | 0.0141 | 0 | 0
Current M | 0.17255 | 0.11318 | 0.0587 | 0.020093
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.575 | 0.39167 | 0.15833 | 0
Proposed M | 0.7139 | 0.4017 | 0.1629 | 0.049
Current M | 0.77244 | 0.76686 | 0.61688 | 0.37524
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.10833 | 0.016667 | 0 | 0
Proposed M | 0.1537 | 0.0072 | 0 | 0
Current M | 0.22086 | 0.15199 | 0.076353 | 0.024196

## Slide 49
Results:
Case 7:
Case 8:
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.41667 | 0.26667 | 0.058333 | 0
Proposed M | 0.5863 | 0.2709 | 0.0879 | 0.0211
Current M | 0.70009 | 0.65102 | 0.45034 | 0.22064
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.083333 | 0.033333 | 0 | 0
Proposed M | 0.1097 | 0.0036 | 0 | 0
Current M | 0.28423 | 0.20026 | 0.094996 | 0.027667
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.275 | 0.125 | 0.05 | 0
Proposed M | 0.4262 | 0.1472 | 0.0357 | 0.0053
Current M | 0.59989 | 0.49429 | 0.27366 | 0.10071
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.05 | 0.033333 | 0 | 0
Proposed M | 0.0605 | 0.0016 | 0 | 0
Current M | 0.36559 | 0.25539 | 0.11199 | 0.030069

## Slide 50
Results
LT vph | TH vph | Bay length | # of TH lanes | CYCLE | TH GREEN | LT GREEN | Blocakge Prob | LT Capacity | Original LT Capacity | Spillback Prob | TH Capacity | Original TH Capacity
300 | 800 | 4 | 2 | 90 | 28 | 21 | 71.20% | 329 | 467 | 42.70% | 979 | 1244
300 | 800 | 6 | 2 | 90 | 28 | 21 | 42.40% | 380 | 467 | 5.97% | 1207 | 1244
300 | 800 | 8 | 2 | 90 | 28 | 21 | 19.10% | 428 | 467 | 0.00% | 1244 | 1244
300 | 800 | 10 | 2 | 90 | 28 | 21 | 6.53% | 454 | 467 | 0.00% | 1244 | 1244
300 | 700 | 4 | 2 | 90 | 24 | 21 | 62.85% | 341 | 467 | 32.01% | 896 | 1067
300 | 700 | 6 | 2 | 90 | 24 | 21 | 32.83% | 399 | 467 | 3.20% | 1050 | 1067
300 | 700 | 8 | 2 | 90 | 24 | 21 | 12.69% | 440 | 467 | 0.02% | 1067 | 1067
300 | 700 | 10 | 2 | 90 | 24 | 21 | 3.78% | 458 | 467 | 0.00% | 1067 | 1067
300 | 600 | 4 | 2 | 90 | 24 | 22 | 45.80% | 384 | 489 | 21.74% | 951 | 1067
300 | 600 | 6 | 2 | 90 | 24 | 22 | 18.06% | 446 | 489 | 0.19% | 1066 | 1067
300 | 600 | 8 | 2 | 90 | 24 | 22 | 5.36% | 476 | 489 | 0.00% | 1067 | 1067
300 | 600 | 10 | 2 | 90 | 24 | 22 | 0.12% | 486 | 489 | 0.00% | 1067 | 1067
300 | 500 | 4 | 2 | 90 | 21 | 22 | 28.12% | 421 | 489 | 12.50% | 875 | 933
300 | 500 | 6 | 2 | 90 | 21 | 22 | 8.42% | 469 | 489 | 0.07% | 933 | 933
300 | 500 | 8 | 2 | 90 | 21 | 22 | 1.80% | 484 | 489 | 0.00% | 933 | 933
300 | 500 | 10 | 2 | 90 | 21 | 22 | 0.00% | 489 | 489 | 0.00% | 933 | 933
200 | 800 | 4 | 2 | 90 | 27 | 16 | 81.31% | 219 | 356 | 19.58% | 1083 | 1200
200 | 800 | 6 | 2 | 90 | 27 | 16 | 52.90% | 261 | 356 | 1.41% | 1192 | 1200
200 | 800 | 8 | 2 | 90 | 27 | 16 | 26.38% | 308 | 356 | 0.00% | 1200 | 1200
200 | 800 | 10 | 2 | 90 | 27 | 16 | 9.81% | 337 | 356 | 0.00% | 1200 | 1200
200 | 700 | 4 | 2 | 90 | 26 | 16 | 71.39% | 229 | 356 | 15.37% | 1067 | 1156
200 | 700 | 6 | 2 | 90 | 26 | 16 | 40.17% | 283 | 356 | 0.72% | 1151 | 1156
200 | 700 | 8 | 2 | 90 | 26 | 16 | 16.29% | 326 | 356 | 0.00% | 1156 | 1156
200 | 700 | 10 | 2 | 90 | 26 | 16 | 4.90% | 346 | 356 | 0.00% | 1156 | 1156
200 | 600 | 4 | 2 | 90 | 24 | 16 | 58.63% | 250 | 356 | 10.97% | 1008 | 1067
200 | 600 | 6 | 2 | 90 | 24 | 16 | 27.09% | 305 | 356 | 0.36% | 1065 | 1067
200 | 600 | 8 | 2 | 90 | 24 | 16 | 8.79% | 339 | 356 | 0.00% | 1067 | 1067
200 | 600 | 10 | 2 | 90 | 24 | 16 | 2.11% | 351 | 356 | 0.00% | 1067 | 1067
200 | 500 | 4 | 2 | 90 | 22 | 16 | 42.62% | 276 | 356 | 6.05% | 948 | 978
200 | 500 | 6 | 2 | 90 | 22 | 16 | 14.72% | 328 | 356 | 0.16% | 977 | 978
200 | 500 | 8 | 2 | 90 | 22 | 16 | 3.57% | 348 | 356 | 0.00% | 978 | 978
200 | 500 | 10 | 2 | 90 | 22 | 16 | 0.53% | 354 | 356 | 0.00% | 978 | 978

## Slide 51: Findings and conclusions
Findings:
For blockage situation:
  a) the length of left-turn bay , the probability ;
  b) the through traffic volume , the probability ;
  c) the left-turn traffic volume , the probability .
Chart: LT: 300 TH: 600
| 4 | 6 | 8 | 10
Simulation | 0.48333 | 0.30833 | 0.075 | 0
Chart: 
| 500 | 600 | 700 | 800
 | 0.275 | 0.41667 | 0.575 | 0.675
Chart: 
| 200 | 300
TH:500 | 0.125 | 0.14167
TH:600 | 0.26667 | 0.30833
TH:700 | 0.39167 | 0.35833
TH:800 | 0.54167 | 0.48333

## Slide 52: Findings and conclusions
Findings:
For spillback situation:
  a) the length of left-turn bay , the probability ;
  b) the left-turn traffic volume , the probability ;
  c) the though traffic volume , the probability .
Chart: 
| 4 | 6 | 8 | 10
Simulation | 0.35833 | 0.066667 | 0.0083333 | 0
Chart: 
| 500 | 600 | 700 | 800
 | 0.05 | 0.083333 | 0.10833 | 0.13333
Chart: 
| 200 | 300
TH:500 | 0.05 | 0.083333
TH:600 | 0.083333 | 0.11667
TH:700 | 0.10833 | 0.25833
TH:800 | 0.13333 | 0.35833

## Slide 53: Findings and conclusions

## Slide 54: Findings and conclusions
Conclusions
The proposed model considers factors and natures that have not been included into the current models;
The proposed model shows better results compared with current models;
The proposed model needs more detailed input and assumptions.

## Slide 55: Limitations and future work
Limitations
No field data for the validation;
No data for the capacity validation;
Arrival patterns are assumed to be Poisson distribution, however in reality, the coming vehicles may not follow this assumption;
The proposed method is not easy to apply, because it needs some iterations to get the stable condition;
The proposed method doesn’t consider the heavy traffic condition, which may cause the residual queue for through traffic after the green time;
The estimation of arrival rate for through traffic in adjacent through lane may need to consider more factors.

## Slide 56: Limitations and future work
Future work
Try to collect some field data and try to find ways to obtain the probabilities of blockage and spillback;
Try to figure out how to validate the capacity results from the model.
Try to enhance the estimation model about the arrival rate for through traffic in adjacent through lane;
Try to consider the heavy traffic condition into the model;
Try to consider the mixed vehicles(buses, trucks) into the model.

## Slide 57
Thank you!