## Slide 1: Applied Technology and Traffic Analysis Program(ATTAP) MIDCAP & MUID
Center for Traffic Safety and Operations
Dept. of Civil and Environmental Engineering
University of Maryland, College Park
Traffic Development & Support Division
Office of Traffic & Safety
Maryland State Highway Administration

## Slide 2: CONTENTS
1
MIDCAP
2
MUID

## Slide 3: MIDCAP
Maryland Intersection and Interchange Design & Capacity Analysis Program

## Slide 4: INTRODUCTION
Maryland Intersection and Interchange Design & Capacity Analysis Program (MIDCAP)
Developed by University of Maryland, College Park and MDSHA
A tool to conduct a capacity/ queuing analysis for signalized intersections and interchanges, signal warrant and shoulder bypass analysis at the preliminary, planning, or design stage
Ok
Ok

## Slide 5: MODULES
Capacity and queue analysis
  for signalized Intersections
  for signalized interchanges
Signal Warrant
Shoulder Bypass Lanes (SBLs) Warrant

## Slide 6: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Uses the CLV method and MDSHA’s Queuing analysis procedure
Provides the volume-to-capacity ratio and corresponding level of service associated with a particular intersection/interchange design, given hourly turning movement volumes, lane configurations, right turn restrictions, and phase control (split or non-split)
Considers different types of intersection/interchange from conventional design (4 leg, 3 leg, diamond intersection) to unconventional design (Continuous Flow Intersection, Single Point Urban Interchange, and Diverging Diamond Interchange)

## Slide 7: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Framework
Calculate Max. queue length
Calculate CLV for each approach
Determine critical movement and calculate intersection CLV
Intersection Critical Lane Volume
Intersection v/c and LOS
Maximum Queue Length
Calculate v/c and determine LOS
Movement volumes
Lane configuration
Intersection type
Right-turn restriction
INPUT
OUTPUT

## Slide 8: MODULE 1: CAPACITY AND QUEUE ANALYSIS
User-friendly interface
2
3
4
5
6
1
1
Choose Intersection Type
Set Lane Configurations
2
Input Movement Volumes
3
Choose Right Turn Control Type
4
Calculate Critical Lane Volume
5
Obtain Intersection LOS & V/C
6

## Slide 9: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Multiple intersections analysis
  Corridor analysis
  Up to 10 intersections

## Slide 10: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Integration of intersection and interchange designs
  On the multiple intersection analysis
Interchange
Intersections

## Slide 11: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Analysis for both AM and PM peak hours at a time

## Slide 12: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Multi-hour analysis

## Slide 13: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Import a report from Internet Traffic Monitoring System (I-TMS) as traffic volume input

## Slide 14: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Factors and Criteria
  Editable Lane Use Factors, LOS criteria, and PCE values
  Can be applied in different intersections and different approaches
  Default values (see tables)

## Slide 15: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Right turn restriction
  Percentage of no-turn-on-red traffic
  Free right turn
  Right turn overlap

## Slide 16: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Comparison summary

## Slide 17: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Recommended bridge length for DDI design

## Slide 18: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Different intersection and interchange designs
  Full CFI
  Symmetric CFI

## Slide 19: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Different intersection and interchange designs
  Asymmetric CFI
  CFI-T

## Slide 20: MODULE 1: CAPACITY AND QUEUE ANALYSIS
Different intersection and interchange designs
  SPUI
  DDI

## Slide 21: MODULE 2: SIGNAL WARRANT
Uses the Maryland Manual on Uniform Traffic Control Devices (MUTCD) 2011 edition
Investigates the need for a traffic control signal by analyzing related factors such as traffic conditions and physical characteristics of the location
Provides whether the following traffic signal warrant is satisfied at a particular location or not
  Warrant 1. Eight-Hour Vehicular Volume
  Warrant 2. Four-Hour Vehicular Volume
  Warrant 3. Peak Hour
  Warrant 9. Intersection Near a Grade Crossing

## Slide 22: MODULE 2: SIGNAL WARRANT
User-friendly Interface
  Import a turning movement report from Internet Traffic Monitoring System (I-TMS) as input
2
3
1
1
Load Traffic volume data
Set Location-specific Characteristics
2
Click Calculate button
3

## Slide 23: MODULE 2: SIGNAL WARRANT
User-friendly Interface
  Evaluation results for Warrant 1

## Slide 24: MODULE 2: SIGNAL WARRANT
User-friendly Interface
  Evaluation results for Warrant 2

## Slide 25: MODULE 2: SIGNAL WARRANT
User-friendly Interface
  Evaluation results for Warrant 3

## Slide 26: MODULE 2: SIGNAL WARRANT
User-friendly Interface
  Evaluation results for Warrant 9

## Slide 27: MODULE 3: SHOULDER BYPASS LANES(SBLs)
Using the MDSHA’s application and design guidelines for shoulder bypass lanes (SBLs)
Investigates the need for shoulder bypass lanes and left-turn lanes by analyzing related factors such as traffic conditions and physical characteristics of the location
Provides whether the following shoulder bypass lane warrant is satisfied at a particular location or not
  Warrant 1. Vehicular Volumes
  Warrant 2. Stopping Sight Distance
  Warrant 3. Accident History

## Slide 28: MODULE 3: SHOULDER BYPASS LANES(SBLs)
User-friendly Interface
2
3
1
1
Input Traffic volume data
Set Location-specific Characteristics
2
Click Calculate button
3

## Slide 29: MODULE 3: SHOULDER BYPASS LANES(SBLs)
User-friendly Interface
  Evaluation results for Warrant 1

## Slide 30: MODULE 3: SHOULDER BYPASS LANES(SBLs)
User-friendly Interface
  Evaluation results for Warrant 2 and Warrant 3

## Slide 31: MUID
Maryland Unconventional Intersection Design Analysis Tool

## Slide 32: INTRODUCTION
Maryland Unconventional Intersection Design (MUID) Analysis Tool
Developed by University of Maryland, College Park and MDSHA
A tool to conduct a capacity/ queuing analysis as well as signal optimization for continuous flow intersection (CFI), diverging diamond interchange (DDI), and superstreet intersection
Notes: Intersections/Interchanges

## Slide 33: MODULES
Planning Evaluation Module
  Queue length
  Average Delay
  Critical Lane Volumes (CLVs)
Signal Optimization Module
  Offset
  Cycle length
  g/C ratio
Notes: In the planning evaluation module, add “Queue/link ratio”
In the signal optimization module, may be “green split” is better than g/C ratio
Another module is output module, which shows input parameters, planning evaluation results and signal optimization results

## Slide 34: PLANNING EVALUATION MODULE
Planning Evaluation Procedure
Identifying all factors contributing to the total delay and queue, including external factors such as demand, and internal factors such as intersection geometric features
Generating a comprehensive data set with all identified factors for simulating analysis
Deriving the quantitative relationships between intersection delays and contributing factors
Build simulation models using VISSIM and Calibrate VISSIM parameters with field data
Estimating the impact of queues on the overall intersection performance and developing a set of statistical models for queues length prediction at each critical location
Random sampling of different demand scenarios
Notes: In the third stage, Intersection delays -> performance measures

## Slide 35: PLANNING EVALUATION MODULE
Planning Evaluation Results

## Slide 36: SIGNAL OPTIMIZATION MODULE
Calculate the CLV of each sub-intersection according to the phasing designs
Determine the common cycle length based on the CLV of the most congested sub-intersection
  For each sub-intersection, optimize the green ratio of each phase with the objective of maximizing the capacity of intersection
  Determine the critical traffic paths according to the demand pattern
  Use a modified MAXBAND model to provide progressions to those critical traffic paths so as to optimize the offsets
1
2
3
4
5
Signal optimization Procedure

## Slide 37: SIGNAL OPTIMIZATION MODULE
Signal Optimization Results
Notes: Can you show two functions below?
The synchronized movements are listed on the top left corner
The user may change the green time and then the graph will update automatically, as well as the average delay
I have attached one slide at the end to somehow show the issues.

## Slide 38: INTERSECTION/INTERCHANGE DESIGNS
Cover different intersection/interchange designs
  Continuous Flow Intersection
    CFI-T
    Partial CFI(symmetrical)
    Partial CFI(asymmetrical)
    Full CFI
  Diverging Diamond Interchange
  Superstreet Intersection

## Slide 39: INPUT DEMAND
User-friendly Interface
  Manually input demand or
  Generate random demand

## Slide 40: INPUT GEOMETRIC CHARACTERISTICS
User-friendly Interface
  Manually input geometric information or
  Generate random demand
Notes: Generate random demand -> adopt the default geometry setting
I think this interface is user friendly mainly because the link will be colored if the corresponding textbox is being selected. Can you show this in the slides.? I have attached one page at the end of this file showing this advantage. It is from the slides for the Utah conference.

## Slide 41: OUTPUT
Show demand

## Slide 42: OUTPUT
Show link length

## Slide 43: OUTPUT
Show phase plan

## Slide 44: OUTPUT
Show Queue length

## Slide 45: OUTPUT
Show Queue/Link length ratio

## Slide 46: OUTPUT
Show signal timing(s)

## Slide 47: OUTPUT
Generate a report with input and module output
Notes: Generate a comprehensive report containing all the input and output of the intersection

## Slide 48: Step 5: Signal Optimization
Optimization for cycle length, green split and offset

## Slide 49: Step 3: Edit Geometric Parameters
Change # of lanes and link Length
The selected link will be colored for convenience