## Slide 1: A bus-based progression system for arterials with heavy transit flows
Geometry information from Liufang Ave. North in Beijing
Green phase (s): 99,77,66,75,60
Dwell time distribution: N (30,9), N (27,7), N (24,6)
Maximal bandwidth: 50s
Models to be evaluated
  Model-1: MAXBAND
  Model-2: an extension of MAXBAND with avg. dwell time
  Model-3: the proposed model
by Yao Cheng, Xianfeng Yang, Gang-Len Chang
University of Maryland, College Park
Abstract
Conventional Transit Signal Priority (TSP) controls often reach a limitation for arterials accommodating heavy bus flows since the priority function can significantly increase delay at minor streets.
To improve reliability of bus operations and increase the bus ridership, a bus-based progression model that considers the operational characteristics of transit vehicles is developed.
The VISSIM simulation with an arterial consisting of five intersections and three two-way bus stops demonstrates that the proposed model can significantly reduce bus passenger delay and the per person delays for the entire arterial.
Research Background
TSP and passive control strategies
TSP has been recognized as a promising method to reduce bus travel time. It responds to the presence of buses and is proven to be effective under low bus demand conditions.
However, at arterials with heavy bus volumes, TSP may reach its limit since 1) most TSP focuses on isolated intersections, and 2) the effectiveness of TSP will be diminished by the increasing number of priority calls.
Passive control strategies may serve as a potentially effective way to deal with arterials with heavy transit flows. But most studies also focus on isolated intersections.
Research Objective
An efficient transit progression model is developed, which fully considers the bus operational features.
The proposed model (Model-3) can outperform Model-2 in terms of reducing the average bus delay (15.25%) and average person delay (14.00%).
Further sensitivity analysis indicates that the model is quite robust when two control parameters vary within a range.
Exploring a better method to analyze the stochastic nature of dwell time may be a future research direction.
Problem Nature
Different from the design of progression for passenger cars, a transit vehicle may need to dwell at a bus stop for a short time when travelling between intersections. A green band designed for transit vehicles shall fully reflect the impact of bus dwell time.
Model Formulation
To overcome these critical issues listed above, this study introduces a variable-band progression model that takes each bus stop as a control point.
Control Objective
Constraints
Interference constraints and progression constraints
Bandwidth constraints
This group of constraints is introduced to make sure that the bandwidths at the upstream intersections of bus stops will be less than a predetermined upper bound.
Case Study and Conclusions
Variable green bands using bus stops as control point
Notably, bus dwell time is dependent on the varying level of passenger demand at bus stops. As shown in most field data, bus dwell time is not a constant, but is stochastic in nature. Hence, failing to fully account for such uncertainty, a transit vehicle may not stay within the preset green band after departing from bus stops.
For both operational and safety concerns, another critical issue to be addressed in design of bus progression system is the storage capacity at bus stops. When the number of arriving buses within a short time period exceeds the storage capacity of a bus stop, the queuing buses may spillback to the nearby intersection and thus block the traffic flows at that intersection. Hence, to prevent the occurrence of such queue spillback, one shall pre-determine an upper bound for bus bandwidth so as to limit the number of buses concurrently arriving at the same stops.
Bus dwell time at stop-3 & 4 of Jiefang Rd, Jinan China collected between 11/01/2012 and 11/07/2012
The proposed model is formulated with a Mixed-Integer-Linear Programming method to optimize the offsets.
The first two are for the outbound direction, where xi is a binary variable. No matter what xi equals, only one of them is effective, ensuring that half of the bandwidth will be less than half of its upper bound. Different values of xi indicate whether the band is close to the start or the end of the green phase.
Constraints accounting for bus dwell time uncertainty
To keep vehicles (within band αbi) entering from the upstream green band to stay within the downstream green band bi+1, the following constraints shall be satisfied:
where, μ denotes the mean bus dwell time and ε denotes its uncertainty; α is a conservative parameter which represents the portion of effective bandwidth for the upstream bus band. By integrating them and defining βσ=|2ε|, one can get:
where, β is a control parameter which indicates the preferred confidence level.
Model-2
Model-3