## Slide 1: Design of a Dilemma Zone Protection System US 40 @ MD 910C (Western Maryland Parkway)
Traffic Safety and Operations Lab

## Slide 2: Outline
Location overview
Accidents history
Field data collection
Speed profiles
Acceleration and deceleration rates
Protection design concept
System components
Proposed design layout

## Slide 3: Location Overview
US 40@ Western Maryland Parkway
  4 lanes divided highway (US 40), 3 approach lanes for Western Maryland Parkway (2-left, 1-right)
  Isolated intersection
  55 mph speed limit
  Ramp from I-81 for eastbound
  5% HV
US 40
MD 910C
US 40
MD 910C
Notes: This location has high truck percentage (14%) also sights are block by Sign for southbound and eastbound approaches
The southbound has grade of +1.4% l from 1000 to the intersection. This also cause the truck driver not to stop… (maybe)

## Slide 4: Accidents History
Historical accidents data (2011 ~2013)
  7 crashes potentially related to dilemma zone decisions for 3 years
  3 injuries
Accident history diagram

## Slide 5: Field Data Collection
4 video camcorders with two reference points
  850 ft, 650ft, 500 ft, and 300ft
1 camcorder for the stop line and the signal
Data Collection Period
  Oct 10th 2014 from 11:30 AM to 12:30 PM and 3:00 PM to 6:00 PM
Data Processing
  Video times are synced with the GPS satellite time
  Exact times to reference points are extracted from videos
900 ft video capture
signal video capture

## Slide 6: Field Data Summary
Speed Profiles (preliminary data collection)
Location | 900 ft | 500 ft | 200 ft
Average speed (mph) | 49.7 | 46.4 | 40.0
Minimum speed (mph) | 18.9 | 10.9 | 4.58
Maximum speed (mph) | 74.1 | 69.4 | 61.2
Sample Size | 1233 | 1371 | 1343
Chart: Speed Profile
| 900 | 500 | 200
Average speed (mph) | 49.7 | 46.4 | 40
Minimum speed (mph) | 18.9 | 10.9 | 4.58
Maximum speed (mph) | 74.1 | 69.4 | 61.2

## Slide 7: Dilemma Zone Distribution
Driver Reaction Time | 1.14sec
Driver Reaction Lag | 1.14sec
Vehicle Length (Passenger Car) | 12ft
Vehicle Length (Heavy Vehicle) | 60ft
Yellow Duration | 5.0sec
Intersection Width | 122ft
Other Parameters-(Default Value)
 | Acceleration Rate () | Deceleration Rate ()
Average (Passenger Cars) | 3.79 | -9.33
Average (Heavy Vehicles) | 2.1 | -9.2
Median | 2.96 | -8.80
Minimum | 0.1 | -2.07
Maximum | 12.27 | -26.80
Average (Passenger Cars) | 3.79 | -9.33
Average (Heavy Vehicles) | 2.1 | -9.2
Median | 2.96 | -8.80
Minimum | 0.1 | -2.07
Maximum | 12.27 | -26.80
Acceleration and Deceleration

## Slide 8: Dilemma Zone Distribution (passenger cars only) (Theoretical Acceleration/Deceleration Rates –AASHTO)
Range need to be covered by the detection system
749ft
445ft
Acceleration rate | 10.00 ft/s2
Deceleration rate | -11.20 ft/s2
Intersection Width | 122ft
Vehicle Length (Passenger Car) | 12ft
Yellow Duration | 5.5sec
Driver Reaction Time | 1.14sec
Notes: Revised

## Slide 9: Dilemma Zone Distribution (passenger cars only) (Average Acc./Dec. Rates from field)
Range need to be covered by the detection system
Average acceleration rate | 3.79ft/s2
Average deceleration rate | -9.33ft/s2
Intersection Width | 122ft
Vehicle Length (Passenger Car) | 12ft
Yellow Duration | 5.5sec
Driver Reaction Time | 1.14sec
872ft
103ft
Deceleration Rate (ft/s^2) Passenger cars only | 
Average | -9.33
std | 5.07
Max | -26.80
Min | -2.07
Median | -8.80
85th percentile | -13.24
# of record | 74
Notes: Revised

## Slide 10: Dilemma Zone Distribution ( For heavy trucks only) (Using Average Acc./Dec. Rates)
Range need to be covered by the detection system
603ft
40ft
38mph
Average acceleration rate | 3.79ft/s2
Average deceleration rate | -9.20t/s2
Intersection Width | 122ft
Vehicle Length (Passenger Car) | 12ft
Yellow Duration | 5.5sec
Driver Reaction Time | 1.14sec
Deceleration Rate (ft/s^2) trucks only | 
Average | -9.20
std | 6.16
Max | -25.83
Min | -2.20
Median | -7.25
85th percentile | -12.60
# of record | 14

## Slide 11: Recommended Dilemma Zone Distribution (Average acc./Dec. Rates from passenger cars and from trucks)
Range need to be covered by the detection system due to large percentage trucks
872ft
40 ft
Combination of DZ distributions
of heavy vehicles and
Average passenger cars
Avg. acceleration rate | 3.79ft/s2
Avg. deceleration rate | -9.33ft/s2
Avg. acceleration rate (Truck) | 3.79ft/s2
Avg. deceleration rate (Truck) | -9.20t/s2
Intersection Width | 122ft
Vehicle Length (Passenger Car) | 12ft
Yellow Duration | 5.5sec
Driver Reaction Time | 1.14sec

## Slide 12: Design Concept
Advanced warning sign with speed control
Microwave detector
Signal Controller
Detection Zone
Location of AWS with flasher
Upper limit from the distribution of DZ (field data)
Speed, location, arrival time
Activation and deactivation of the message sign
Signal control includes all-red extension
Advisory SPEED
50
PREPARE TO STOP WHEN FLASHING

## Slide 13: System components
Connection Module
(click 223 301)
Connection Module
(click 223 112)
Lab (monitoring)
Wireless Modem
Wireless connector
Wireless connector
Microcontroller
Advisory SPEED
55
PREPARE TO STOP WHEN FLASHING
I.e. Panasonic toughbook
i.e. Raven X modem
Two Smartsensor Advanced
Option 1
Real-time Monitoring
Option 2
Advanced Warning
Econolite ASC/3

## Slide 14: Major System Components
Sensor(s) for dilemma zone protection
  Microwave long range detector (Smartsensor Advanced Extended Range)
  can cover up to the upper limit of DZ
  Provides real-time traffic data (speed, location) over each sliced interval 0.1 second)
Signal controller (Econolite ASC/3)
  Provides all-red extension to the driver who tries to run over the all-red phase
SmartSensor Advance extended range
Up to 600 ft detection for motor vehicle
Up to 900 ft detection for HV
Econolite ASC/3

## Slide 15: Real-Time Monitoring System
PC
  Harden PC can be stored in cabinet (i.e. Panasonic toughbook)
  Store and send the log file to the Lab
Modem
  Wireless communications (i.e. Raven X modem)
Connection Module
  Allow additional connections to sensors (i.e. Click 301)
  Surge protection (i.e. Click 223)
In cabinet PC
i.e. Panasonic toughbook
Wireless Modem
i.e.Raven X modem
Connection module
i.e. Click 301 (Wavetronix)
Real-time monitoring
Surge Protection
i.e. Click 223 (Wavetronix)

## Slide 16: AWS system
Advanced warning sign
  Activated when the signal changes to the yellow
  Location ()
: perception-reaction time (1.5 seconds);
: vehicle speed.
Advisory speed
  Advisory speed for vehicles to safely stop ahead of the stop line
RF signal transmitter
  Send the activation/deactivation signal to AWS (i.e. RF Data Transceiver: SSRT-09-RS485)
Microcontroller
  Receive signals via the wireless connection to control AWS
  * Wireless connections can be replaced with wire connections
Microcontroller
(activate AWS)
PREPARE TO STOP WHEN FLASHING
Wireless
Wireless communication
i.e. RF Data Transceiver: SSRT-09-RS485
ASC/3

## Slide 17: List of Equipment
Smartsensor Advanced Extended Range
  Transportation Equipment & Services, Inc.
Econolite ASC/3
  Econolite
Laptop
  Panasonic Toughbook CF-53 CF-53SJCZYLM ( CF-53SJCHYLM )
    http://toughruggedlaptops.com
Raven X modem
  Raven Series - Proven, 2G/3G gateway (Raven XE)
    http://www.sierrawireless.com/
Click 223, 301
  Transportation Equipment & Services, Inc.
RF Data Transceiver: SSRT-09-RS485
  http://www.abacom-tech.com
Major Component
Monitoring Module
AWS
Module

## Slide 18: All-Red Extension operational flow chart
All red phase starts
Update AR
AR = AR + extension
Any vehicle above the thresholds and AR extendable?
Does vehicle can clear the intersection without extension?
T = 0
AR = all red
T < AR?
T = T + 0.1
End All red
YES
YES
NO
NO
YES
NO
Vehicle Speed | Distance to stop line
>= 35 mph | < 200 ft
>= 45 mph | < 300 ft
>= 55 mph | < 450 ft
>= 65 mph | < 600 ft
> = 75 mph | Any detection zone
Extension Criteria
  During the all-red phase
    If any vehicles are detected above the threshold in the detection zone, the controller will activate the all-red extension until the target vehicles have passed the intersection

## Slide 19: Proposed Design (Type-1:AWS only)
Advanced warning sign
Signal Controller
Detection Zone
Two microwave detectors (0-500 and 500-900 feet)
PREPARE TO STOP WHEN FLASHING
900 feet
Microwave sensor (0-500 ft)
Microwave sensor (500-900 ft)
1050 feet
Recommended detection zone range
Location of sign
Detection Zone
500 feet
400 feet

## Slide 20: Proposed Design: Type 2 (AWS with speed limit)
Advanced warning sign with Posted Speed Limit
Signal Controller
Detection Zone
500 feet
900 feet
Microwave sensor (0-500 ft)
Two microwave detectors (0-500 and 500-900 feet)
Microwave sensor (500-900 ft)
PREPARE TO STOP WHEN FLASHING
1050 feet
Recommended detection zone range
Location of sign
Detection Zone
400 feet

## Slide 21: Proposed Design: Type 3: (AWS with speed limit)
Advanced warning sign with advisory speed Limit
Signal Controller
Detection Zone
500 feet
900 feet
Microwave sensor (0-500 ft)
Two microwave detectors (0-500 and 500-900 feet)
Microwave sensor (500-900 ft)
1050 feet
Recommended detection zone range
Location of sign
Detection Zone
400 feet
Advisory SPEED
50
PREPARE TO STOP WHEN FLASHING