## Slide 1
Drone
As a Tool For Traffic Engineering

## Slide 2
Outline
7
2
3
4
5
6
1
Introduction of Drone
Applications of Drone in Civil Engineering
Applications of Drone in Traffic Engineering
Regulations for Drone Operation
The Operation of Drone for Traffic Engineering
Data Processing Software
Selections of Drone
8
Insurance
9
Case Study

## Slide 3
Drone –> Small Unmanned Aerial System (sUAS)
Small unmanned aerial system (sUAS) is categorized as drones less then 55 lbs.
In 2019, 36 out of 50 state DOTs funded centers or programs for drone operations
Introduction of Drone

## Slide 4
Introduction of Drone – Components of Drone
Text Here
Aircraft
Ground Station
  Remote Controller
  Data Processing
Payload
  Camera
  Gimbal

## Slide 5
Categories of Drones
  Fixed wing
  Multi-rotor
    Tethered Drone
      Drone with cable connected to ground station
    Untethered Drone
      Drone without cable connected to ground station
Introduction of Drone – Categories of Drone
Maneuverability |  | 
Price |  | 
Ease-of-use |  | 
Operation Range |  | 
Stability |  | 
Payload Capacity |  | 
Efficiency for Mapping |  | 

## Slide 6
Search and Rescue (SAR)
Damage Evaluation and Assessment
Rapid Service Recovery.
Public Safety and Disaster Management
Infrastructure Maintenance
  Cyberhawk – oil, gas, and wind turbine structure inspection
Construction Management
  Truebeck – new Uber’s headquarter construction project
Construction
Traffic Engineering
Applications of Drone in Civil Engineering
Drone can be used in several civil applications due to their ease of deployment, low maintenance cost, high mobility, and hovering ability (Shakhatreh et al., 2018)
Bridge and road infrastructure inspection
Traffic Management
  Data Collection
  Traffic Monitoring and control
  Parking Lot Utilization

## Slide 7
  Narrow observation range
  High cost to cover the huge network
  Low flexibility for emergent events
Applications of Drone in Traffic Management
What are the limitations and drawbacks of fixed cameras?
sourced from: https://www.youtube.com/watch?v=MNn9qKG2UFI&t=4s
Drone can free us from the limitations

## Slide 8
Applications of Drone in Traffic Management
  Traffic Monitoring
    Traffic Flow Parameters
    Queue Length
    Vehicular Trajectories
  Path Flow Calculation
    Traffic Counting
    Pedestrians and Cyclists Behavior
Data Collection
Parking Lot Utilization
Reference: Sutheerakul, et al., 2016, Data From Sky, 2019

## Slide 9
Regulations for Drone Operation
Visual-line-of-Sight (VLOS) only.
Max. Ground Speed = 100mph
Max. Altitude = 400ft
Not operate directly over people
Remote Pilot Certification required
Min. weather visibility from control station = 3 miles
Aircrafts need to be officially registered and marked
sUAS (for drone less than 55 lbs.) is governed under FAA Part 107.
Daylight or Civil Twilight only
Flight beyond FAA Part 107, Wavier Authorization required

## Slide 10
Regulations for Drone Operation – Remote Pilot Certification
Schedule an appointment with a Knowledge Testing Center and pass the Aeronautical Knowledge Test
Complete FAA Form 8710-13 for a remote pilot certificate in IACRA System
Valid for 2 years, holders must pass a recurrent knowledge test every 2 years

## Slide 11
Regulations for Drone Operation – Restricted Area
DC is governed by SFRA within a 30-mile radius of Ronald Reagan Washington National Airport (DCA)
Inner ring (15-miles radius): Prohibited to fly without specific FAA authorization
Outer ring (15-30 miles radius): Allow to fly under Part 107
Washington D.C (Special Use Airspace)
Must get permission from ATC (Air Traffic Control) if the pilots hold remote pilot certification
Flying Near Airport (Class B, C, D, E)
UAS is prohibited within the 3-miles radius of stadium or venue without authorization
Stadium and Sport Events
Military based
National landmarks
Certain critical infrastructure (Nuclear Power Plants)
Other Restricted Area

## Slide 12
Maryland State
Regulations for Drone Operation – Restricted Area
sourced from: https://www.airmap.com/
15 miles radius of Washington D.C
Class B and Class D airspace, represent key and moderate used airports
Class E airspace, always represent small airports

## Slide 13
The Operation of Drone for Traffic Management
1st
2nd
3rd
Inspection prior to fight (Part 107)
Schedule of flight route
Flight Planning
Image or Video Capturing
Data Processing
Reference: BestDroneForTheJob, 2019, Data From Sky, 2019
The stability of drone and the camera performance are the critical factor to ensure the high quality of data

## Slide 14
Selections of Drones – Main Criterion
Flight time, Wind persistence, Transmission distance, Operational temperature range, etc.
Operation Parameters
Obstacle sensors, etc.
Operation Safety
Camera sensor, Image or video resolution, Zoom function, etc.
Camera Performance
Place of Production
Price

## Slide 15
Selections of Drones – Decision Matrix for Normal Drones
Criterion | Operation Parameters | Camera Performance | Operation Safety | Price | Place of Production | Total Score
Weight | 10 | 10 | 10 | 6 | 9 | 
DJI - Mavic Pro | 10 | 10 | 9 | 6 | 7 | 389
DJI - Mavic Zoom | 10 | 10 | 9 | 7 | 7 | 396
DJI - Mavic Pro Platinum | 10 | 8 | 8 | 8 | 7 | 371
Parrot - Annafi | 9 | 10 | 6 | 10 | 9 | 391
Autel Robotics - EVO | 9 | 8 | 9 | 9 | 8 | 386
Skydio - Skydio 2 | 7 | 10 | 10 | 8 | 10 | 408
GDU - O2 Plus | 6 | 8 | 9 | 10 | 8 | 362
GDU - Byrd Premium 2.0 | 8 | 8 | 8 | 9 | 9 | 375

## Slide 16
Skydio 2
Operation Parameters | 
Flight Time | 23 mins
Max. Wind Speed | 12 m/s
Transmission Distance | 3.5 km
Camera Performance | 
Camera Sensor | 45 MP
Image Resolution | 4K, 60fps
Gimbal Axis | 3-axis
Operation Safety | 
Obstacle Sensor | 360° Obstacle Sensor
Price | 
US$ 1,299 | 
Fully Autonomous Drone
Reference: Skydio Skydio 2, 2019

## Slide 17
Selections of Drones – Decision Matrix for Professional Drones
Criterion | Operation Parameters | Camera Performance | Operation Safety | Price | Place of Production | Total Score
Weight | 10 | 10 | 7 | 8 | 10 | 
3DR – H520G | 8 | 8 | 10 | 10 | 10 | 410
Impossible Aerospace – US-1 | 10 | 9 | 9 | 9 | 10 | 425
Aerialtronic – Zenith | 9 | 10 | 9 | 7 | 9 | 399
Freefly – Alta 8 | 8 | 8 | 9 | 8 | 10 | 387
Intel – Falcon 8+ | 8 | 9 | 9 | 8 | 10 | 497

## Slide 18
Impossible Aerospace
Operation Parameters | 
Flight Time | 78 mins
Modes | Auto-takeoff, Return-to-home
Camera Performance | 
Camera Selection | Flir Duo Pro R Thermal
Image Resolution | 4K, 30fps
Gimbal Axis | 3-axis
Extra | Thermal Camera Equipped
Operation Safety | 
Obstacle Sensor | No
Price | 
US$ 19,999 | 
Reference: Impossible Aerospace US-1, 2019

## Slide 19
Elistair – Orion
Operation Parameters | 
Flight Time | Unlimited
Modes | Auto-takeoff, Return-to-home
Operating Altitude | 80m / 262feet
Camera Performance | 
Camera Selection | YRIS Z36
Image Resolution | 1080p, 30fps
Gimbal Axis | 3-axis
Zoom | X36 Zoom
Operation Safety | 
Ground station | Safety switch included
Price | 
US$ 75,000 with whole system | 
Reference:Elistair, 2019
Tethered Drone for
Long time data collection

## Slide 20
Insurance
This coverage will protect the business from Property Damage and Bodily Injury claims that may arise through the commercial operation of UAS.
Liability
Hull coverage’s purpose is protecting the business from the financial cost from any Physical Damage that may occur to its UAV(s).
Hull
This coverage is designed to protect the insured from any Physical Damage losses to a scheduled payload and ground equipment.
Payload and Ground Equipment

## Slide 21
Insurance
The insurance depends on:
Detailed information about the drone
  Specific function
  Cost of the drone and each extra equipment
Main operational needs
Place in which drones operate
Remote Pilot Certification
Types of Insurance
Long-term insurance
  Annually
  Run as little as around $500-750 a year
Short-term insurance
  On-demand
  Run as little as $5-10 per hour

## Slide 22
Data Processing Platform
Road Users Identification and Classification
Traffic Counts, Turning Movement, OD-matrix
Speed, Acceleration, Vehicular Trajectories
Parking Lot Detection
What can drones achieve?
Accuracy of Data – More than 95%

## Slide 23
Data Processing Software
With the data with high quality collected by drone, some traffic research can be carried out:
Motion pattern classification, abnormal motion pattern detection
  Traffic mining
  Trajectory clustering
Traffic safety analysis and improvement
  Driver decision making analysis
  Road user interaction, multi-actor interactions, traffic instabilities
  Prediction of non-recurrent short-term traffic patterns
Comparison of simulation models

## Slide 24
Case Study
Ohio State University (2003)
Drone: MLB BATIII with two video cameras
Level of Service (LOS) and Average Annual Daily Travel (AADT)
  Series of Frames
Queue Length
Origin-Destination Estimation
Parking Lot Utilization
Northbound flight over SR315 for 20s, extracted vehicular trajectories for the Southbound traffic
Drone circled an individual intersection for several minutes
Drone circled above i6 and i7 and cooperated with ground camera to create OD matrix
Drone was devoted to flying over several parking lot in the last few minutes of flight
Total Estimated Cost of the Project: About US$50,000 in 2005 ($48,000 for the Drone)

## Slide 25
Case Study
Michigan Tech Research Institute – MDOT (2015-2018)
Bridge and Road Inspection
Traffic Monitoring
  Drone: DJI Mavic
    Each flight less than 10 mins
  Semi-automated UAV traffic monitoring
    Input landmark information and label an object of interest
      Traffic flow parameters
      Time-space vehicular trajectories
Price for the Drone in traffic monitoring: About US$ 1,000

## Slide 26
Dataset for Naturalistic Driving Behavior
HighD (2018)
Tracking Accuracy
  Track Mean Speed Distribution
  Truck Ratio
HighD – Data Accuracy
  99% of vehicles are detected
  Mean position errors are below 3cm

## Slide 27
Conclusion
Under Part 107’s regulation of flight altitude, the max. observation range of drone can cover one huge intersection
  Multiple drones operating at the same time can create a bigger network
To satisfy the applications of traffic engineering, camera performance is the critical issue
  As a tool for data collection, normal drones are fairly good enough
Advantages of drones include:
  Able to provide boarder investigation area
  High flexibility and mobility
  Able to derive more aspects of traffic data
  Time saving for collecting traffic data
Disadvantages of drones include:
  Highly qualified pilots required for safe operations
  The sensitivity of the security issue
  Most of drones cannot provide long flight duration

## Slide 28
References
AASHTO. 2018. Survey Finds a Growing Number of State DOTS Are Deploying Drones to Improve Safety and Collect Data Faster and Better – Saving Time and Money. [Online]. [Accessed 13 October 2019]. Available from: https://adobeindd.com/view/publications/12579497-56a5-4d8a-b8fe-e48c95630c99/1/publication-web-resources/pdf/Drones'18cc.pdf
AERIALTRONICS. 2019. Altura Zenith. [Online]. [Accessed 6 October 2019]. Available from: https://www.aerialtronics.com/en/products/altura-zenith
Autel Robotics. 2019. EVO. [Online]. [Accessed 9 October 2019]. Available from: https://auteldrones.com/products/evo
Barmpounakis, E., Vlahogianni, E.I., and Golias, J.C. 2016. Unmanned Aerial Aircraft Systems for transportation engineering: Current practice and future challenges. International Journal of Transportation Science and Technology. 5(2016), pp. 111-122.
Brooks, C., Dobson, R., Banach, D., Oommen, T., Zhang, K., Mukherjee, A., Havens, T., Ahlborn, T., Escobar-Wolf, R., Bhat, C., Zhao, S., and Lyu Q. 2018. Implementation of Unmanned Aerial Vehicles ( UAVs) for Assessment of Transportation Infrastructure – Phase II. [Online]. [Accessed 16 October 2019]. Available from: https://trid.trb.org/view/1542464
Coifman, B., McCord, M., Mishalani, R.G., Iswalt, M., and Ji, Y. 2006. Roadway traffic monitoring from an unmanned aerial vehicle. IEEE Proceeding – Intelligent Transport Systems. 153(1), pp. 11-20.
DJI. 2019. DJI. [Online]. [Accessed 9 October 2019]. Available from: https://www.dji.com/
Elistair. 2019. ORION. [Online]. [Accessed 14 October 2019]. Available from: https://elistair.com/orion-tethered-drone/
Federal Aviation Administration. 2019. Unmanned Aircraft Systems (UAS). [Online]. [Accessed 20 October 2019]. Available from: https://www.faa.gov/uas/
FREEFLY. 2019. ALTA 8. [Online]. [Accessed 6 October 2019]. Available from: https://freeflysystems.com/alta-8
GDU. 2019. GUD. [Online]. {Accessed 9 October 2019]. Available from: http://www.gdu-tech.com/en
INTEL.2019. INTEL FALCON 8+ SYSTEM. [Online]. [Accessed 6 October 2019]. Available from: https://www.intel.com/content/www/us/en/products/drones/falcon-8.html

## Slide 29
References (Cont’d)
Impossible Aerospace. 2019. MEET US-1. [Online]. [Accessed 6 October 2019]. Available from: https://www.impossible.aero/us-1/
Katayama, K., Takahashi, H., Yokota, N., Sugiyasu, K., Kitagata, G., and Kinoshita, T. 2019. An Effective Multi-UAVs-Based Evacuation Guidance Support for Disaster Risk Reduction. 2019 IEEE International Conference on Big Data and Smart Computing (BigComp), 27 Feb – 2 March 2019. Kyoto. [Online]. IEEE. [Accessed 17 October 2019]. Available from: https://ieeexplore.ieee.org/document/8679474
Khan, M.A., Ectors, W., Bellemans, T., Janssens, D., and Wets, G. 2017. UAV-Based Traffic Analysis: A Universal Guiding Framework Based on Literature Survey. Transportation Research Procedia. 22(2017), pp.541-550.
Krajewski, R., Bock J., Kloeker, L., and Eckstein, L. 2018. The high-D Dataset: A Drone Dataset of Naturalistic Vehicle Trajectories on German Highways for Validation of Highly Automated Driving Systems. 2018 21st International Conference on Intelligent Transportation Systems (ITSC), 4-7 November 2018. Maui. [Online]. IEEE. [Accessed 16 October 2019]. Available from: https://ieeexplore.ieee.org/document/8569552
McGuire, M., Rys, M., and Rys, A. 2016. A Study of How Unmanned Aircraft Systems Can Support the Kansas Department of Transportation’s Efforts to Improve Efficiency, Safety, and Cost Reduction. [Online]. [Accessed 15 October 2019]. Available from: https://trid.trb.org/view/1420349
Menouar, H., Guvenc, I., Akkaya, K., Uluagac, A.S., Kadri, A., and Tuncer, A. 2017. UAV-Enabled Intelligent Transportation Systems for the Smart City: Applications and Challenges. IEEE Communications Magazine. 55(3), pp. 22-28.
Ni, D., and Plotnikov, M. 2016.The state of the Practice of UAS Systems in Transportation. [Online]. [Accessed 15 October 2019]. Available from: https://rosap.ntl.bts.gov/view/dot/35033
Parrot. 2019. ANAFI. [Online]. [Accessed 9 October 2019]. Available from: https://www.parrot.com/us/drones/anafi
Peng, C.F. Hsieh, J.W., Leu, S.W., and Chuang, C.H. 2018. Drone-Based Vacant Parking Space Detection. 2018 32nd International Conference on Advanced Information Networking and Applications Workshop (WAINA), 16-18 May 2018. Krakow. [Online]. IEEE. [Accessed 16 October 2019]. Available from: https://ieeexplore.ieee.org/document/8418140

## Slide 30
Puri, A. 2005. A Survey of Unmanned Aerial Vehicles (UAV) for Traffic Surveillance.
Shakhatreh, H., Sawalmeh, A., Al-Fuqaha, A., Dou, Z., Almaita, E., Khalil, I., Othman, N.S., Khreishah, A., and Guizani, M. 2019. Unmanned Aerial Vehicles (UAVs): A Survey on Civil Applications and Key Research Challenges. IEEE Access. 7, pp. 48672-48634.
Skydio. 2019. Skydio 2. [Online]. [Accessed 9 October 2019]. Available from: https://www.skydio.com/
Sutheerakul C., Kronprasert, N., Kaewmoracharoen, M., and Pichayapan, P. 2017. Application of Unmanned Aerial Vehicles to Pedestrian Traffic Monitoring and Management for Shopping Streets. 2017. Transportation Research Procedia. 25(2017), pp.1717-1734.
UAV COACH. 2019. Guide. [Online]. [Accessed 1 October 2019]. Available from: https://uavcoach.com/
3DR. 2019. 3DR H520-G. [Online]. [Accessed 6 October 2019]. Available from: https://3dr.com/products/h520g/
References (Cont’d)