## Slide 1: AN INTEGRATED BUS-BASED PROGRESSION SYSTEM FOR ARTERIALS HAVING HEAVY TRANSIT FLOWS
Yao Cheng
11/25/2014
Thesis Defense for the Degree of Master of Science

## Slide 2: Transit Signal Priority (TSP)
Transit system
Active control strategies
Bus-based progression
Bus operational features
Source: Sustainable Transportation in the Netherlands

## Slide 3: Outline
Literature Review
Problem Nature and Modelling Framework
Methodology
Case Study
Conclusions and Future Study

## Slide 4: Literature Review
The concept of TSP has been developed since late 1960s (Smith, 1968).
    Active strategies detect the arrival of buses and grant a priority to them. (Ludwick & John, 1974; Dion & Hesham, 2005)
  Passive strategies do not recognize the presence of buses, but predetermine the signal timings to facilitate bus movements. (Urbanik, 1977)
Limitations of TSP strategies
  Significant negative impact to cross-street traffic if the target arterials experience heavy bus volumes
  May interrupt the conventional signal progression design

## Slide 5: Literature Review
Signal progression, first presented by Morgan and Little (1964), is studied mainly for passenger cars.
  Allow some vehicles to pass consecutive intersections without encountering red phases.
  Reduce accidents
  MAXBAND (Little et al., 1981)
  MULTIBAND (Gartner et al., 1990)
Bus progression is a promising passive strategy to improve the operational efficiency of transit system with
  minimized negative impact to cross-street traffic
  benefits to transit vehicles on an arterial
outbound
inbound

## Slide 6: Outline
Literature Review
Problem Nature and Modelling Framework
Methodology
Case Study
Conclusions and Future Study

## Slide 7: Critical issues
Dwell time at bus stops
Dwell time uncertainty
Bus stop capacity
Competition between buses and PCs

## Slide 8: Critical issues
Dwell time at bus stops
Dwell time uncertainty
Bus stop capacity
Competition between buses and PCs
Transit vehicles, impacted by the dwell time at stops, may not stay in the green band designed for passenger cars.

## Slide 9: Critical issues
Dwell time at bus stops
Dwell time uncertainty
Bus stop capacity
Competition between buses and PCs
Deterministic dwell time VS. Stochastic dwell time
The stochastic nature of bus dwell time should be considered when studying bus progression.

## Slide 10: Critical issues
Dwell time at bus stops
Dwell time uncertainty
Bus stop capacity
Competition between buses and PCs
Is the wider band always better?
The number of buses in a band shall not exceed the capacity of the bus stop to prevent the formation of bus queues.

## Slide 11: Critical issues
Dwell time at bus stops
Dwell time uncertainty
Bus stop capacity
Competition between buses and PCs
The bus band and passenger-car band may need to be optimized concurrently.

## Slide 12: Critical issues
Dwell time at bus stops
Dwell time uncertainty
Bus stop capacity
Competition between buses and PCs
A deterministic model
An evaluation module
Following the concept of MAXBAND, a Mixed-Integer Linear Programming model is developed .
Taking advantage of the results produced from the deterministic model, an evaluation module is developed to fully account for the stochastic nature of bus dwell time.
Modelling Framework
A progression model for buses
An enhanced deterministic model
An enhanced evaluation module
A integrated model for both buses and PC s
Integrating passenger car’s benefits

## Slide 13: Outline
Literature Review
Problem Nature and Modelling Framework
Methodology
Case Study
Conclusions and Future Study
A deterministic model
An evaluation module
An integrated model

## Slide 14: Methodology
Mixed Integer Linear Programming
Objective function
Constraints
  Interference constraints
Discussion of parameter :
is a weight factor
The value of depends on the number of buses passing intersection using the synchronized phase.
A deterministic model
Taking each bus stop as a control point

## Slide 15: Methodology
Constraints
  Progression constraints
    For links with bus stops
      Outbound
      Inbound
    For other intersections
      Outbound
      Inbound
A deterministic model
Average dwell time
Dwell time at bus stops

## Slide 16: Methodology
Constraints (bus stop capacity)
  Bandwidth limit
    Outbound
    Inbound
    These constraints are only for upstream intersections of bus stops
The center of a band
should be either close to the start of green
or close to the end of green
to make sure that the potential band is realistic.
: a predetermined maximum bandwidth
: a big number
: a binary variable
A deterministic model
Bus stop capacity

## Slide 17: Methodology
Other Constraints
  Bandwidth equality
    For links without bus stops
  Dwell time uncertainty
    For links with bus stops
A deterministic model
For those buses passing the upstream intersection during , if the dwell time uncertainty is within a specific range, the departing band should accommodate them.
: between 0 and 1
: indicating the tolerance of dwell time uncertainty

## Slide 18
Methodology
A deterministic model
Objective Function
Constraints
Interference constraints
For adjacent intersections between which that a stop is located
Progression constraints
Bandwidth constraints
Dwell time uncertainty
For other intersections
Progression constraints
Bandwidth equality

## Slide 19: Methodology
A deterministic model
An evaluation module
A progression model for buses
An enhanced deterministic model
An enhanced evaluation module
A integrated model for both buses and PC s
Integrating passenger car’s benefits

## Slide 20
Methodology
By adjusting parameters in this critical constraint, one may have multiple sub-optimal solutions.
They will be evaluated and ranked, fully taking the stochastic nature of bus dwell time into consideration.
Upstream
Downstream
An evaluation module

## Slide 21
Methodology
An evaluation module
Computational complexity
Still describing the relation between the arriving bandwidth and the departing bandwidth
Still ensuring a relatively large departing bandwidth based on its arriving bandwidth
Although the dwell time variance is no longer considered in the constraints, the analysis to sub-optimal solutions applies a more rigorous method to assess the impact of dwell time variance
Discussion of parameter :
Different values lead to different “optimal” solution
A Greater value for ensures a higher probability of a bus to keep in the band
A Smaller value for allows a larger arriving bandwidth
A too Large value for leads to meaningless upstream bands.

## Slide 22: Methodology
How effective a signal plan is highly depends on the relation between each pair of bands arriving to and departing from a bus stop.
To evaluate the sub-optimal solutions, this module computes the expectation of the fraction of the arriving bandwidth which can be effectively utilized.
This expectation is called “effective bandwidth”.
An evaluation module

## Slide 23
An evaluation module
Methodology
In order to compute the effective bandwidths, one first needs to calculate the probability of a bus to keep in the band.

## Slide 24
An evaluation module
Methodology
Probability for the bus coming at time x to stay in the downstream band
  For outbound
  For inbound
Calculate the “effective bandwidth”
  is the “effective” part among a short period of time
  The “effective bandwidth” can be calculated by
    For outbound
    For inbound
For an intersection that is not at upstream of a bus stop:
Dwell time uncertainty

## Slide 25
A larger “effective bandwidth” indicates a higher fraction of the buses which can stay in both the arriving and departing bands.
Each solution from the deterministic model will generate effective bandwidths, an outbound one and an inbound one for each intersection, where is the number of intersections.
The solution giving the maximum sum of effective bandwidths can be considered as the optimal solution for the model.
An evaluation module
Methodology

## Slide 26
An evaluation module
Methodology
Cycle length, green split, travel time, estimated bus dwell time….
Each solution has a set of bandwidths and offsets
Find the solution with the maximum total effective bandwidths

## Slide 27: Methodology
A deterministic model
An evaluation module
A progression model for buses
An enhanced deterministic model
An enhanced evaluation module
A integrated model for both buses and PC s
Integrating passenger car’s benefits

## Slide 28
Methodology
An integrated model
Designing bus bands causes potential interruption for passenger car movements.
Even with the same bus bands, the benefit for passenger cars can be different among signal plans.

## Slide 29: Methodology
Therefore, the bus bands and the passenger car bands need to be optimized concurrently.
An integrated model
An enhanced deterministic model
An enhanced evaluation module
Revising the objective function to include bands for both types of vehicles.
Revising the constraints to express passenger car bands.
When comparing the sub-optimal solutions, both effective bandwidths for buses and passenger car bandwidths are considered.

## Slide 30
Objective function
Additional constraints
  To balance the bus bands and the passenger-car bands and avoid one dominating the other,
  Constraints to express passenger-car bands
Methodology
An integrated model
Ratio between numbers of passengers on two types of vehicles
Competition between buses and PCs
An enhanced deterministic model
k<1: Passengers on PCs are less
k>1: Passengers on buses are less

## Slide 31
Enhancement to the stochastic analysis
  The ranking index of a sub-optimal solution includes both effective bandwidth of bus bands and passenger-car bands
Methodology
Total effective bandwidths
Total passenger-car bandwidths
An integrated model
An enhanced evaluation module

## Slide 32
Methodology
Cycle length, green split, travel time, estimated bus dwell time….
Each solution has a set of bandwidths and offsets
Find the solution with the maximum ranking index
An integrated model

## Slide 33: Methodology
A deterministic model
An evaluation module
Following the concept of MAXBAND, a Mixed-Integer Linear Programming model is developed .
By adjusting a parameter in the MILP, multiple sub-optimal solutions will be produced and evaluated, accounting for the stochastic nature of bus dwell time.
A progression model for buses
An enhanced deterministic model
An enhanced evaluation module
A integrated model for both buses and PC s
Integrating passenger car’s benefits
Benefits of both buses and passenger cars are considered.
Dwell time at bus stops
Bus stop capacity
Dwell time uncertainty
Competition between buses and PCs

## Slide 34: Outline
Literature Review
Problem Nature and Modelling Framework
Methodology
Case Study
Conclusions and Future Study

## Slide 35: Case Study
Case Design
Link | Link length (ft) | travel time | With bus stop?
I↔II | 906 | 20 | Yes
II↔III | 948 | 21 | No
III↔IV | 1250 | 28 | Yes
IV↔V | 725 | 16 | Yes
Cycle length is 150 seconds;
Green times at intersections are 99 , 77 , 66, 75, and 60 seconds, respectively;
The dwell time: bus stop 1: N(30,9); bus stop 2: N(27,7); bus stop 3: (24,9);
The bus stop capacity is 2 buses at each direction, and the confidence parameter p equals 0.95; then the maximal bus bandwidth could be computed as 50 seconds
For each direction along the arterial, the bus volume is 60 veh/h, with an average headway of 1.0 minute and the passenger car volume is 750 veh/h;

## Slide 36: Case Study
Models to be evaluated
  Model-1: MAXBAND with fixed phase sequences
  Model-2: A direct extension of MAXBAND by adding the average bus dwell time to the travel time on the links having a bus stop.
  Model-3: The proposed deterministic model
  Model-4: The proposed deterministic model with the evaluation module
  Model-5: The proposed integrated model
The MILP is solved with LINGO. The evaluation module is conducted with R studio.

## Slide 37: Case Study
Task 1: Bandwidths and performance measures generated by bus progression models will first be compared to verify the necessity of the evaluation module.
Task 2: Then the signal plans generated by all Models will be applied in the simulation software, VISSIM, and will be evaluated based on the average delays and number of stops.
Task 3: Sensitivity Analysis will then be conducted with respect to the number of passengers on buses to assess the stability of the proposed integrated model.

## Slide 38: Case Study
MAXBAND with extension
The deterministic model
The deterministic model + the evaluation stage
Fixed bandwidths
Varying bandwidths
Bandwidths limited by the capacity constraints

## Slide 39: Case Study
 |  |  | Offsets (s) at Intersection No. |  |  |  | 
 | α | β | 1 | 2 | 3 | 4 | 5
Model-3-1 | 0.3 | 1 | 0 | 102 | 101 | 40 | 38
Model-3-2 | 0.3 | 2 | 0 | 107 | 104 | 38 | 43
Model-3-3 | 0.5 | 1 | 0 | 105 | 98 | 37 | 41
Model-3-4 | 0 | 1 | 0 | 99 | 104 | 25 | 35
Model-3-5 | 0.1 | 2 | 0 | 104 | 99 | 41 | 40
The deterministic model + the evaluation stage
To verify the necessity of the evaluation module, several sets of parameters for Model-3 are tested.

## Slide 40: Case study
Chart: Avg. Passenger Car Delay (sec)
| Model-1 | Model-2 | Model-4 | Model-5
 | 135.1667 | 117.7167 | 147.55 | 113.9667
Chart: Avg. Bus Delay (sec)
| Model-1 | Model-2 | Model-4 | Model-5
 | 189.3 | 131.25 | 107.9333 | 127.6667
Chart: Avg. per person delay (sec)
| Model-1 | Model-2 | Model-4 | Model-5
 | 164.6939 | 125.0985 | 125.9409 | 121.4394
Chart: Avg. number of stops
| Model-1 | Model-2 | Model-4 | Model-5
 | 2.06 | 2.2 | 2.125 | 2.07
  Model-1: MAXBAND with fixed phase sequences
  Model-2: A direct extension of MAXBAND
  Model-4: The proposed deterministic model with the evaluation ranking stage
  Model-5: The proposed integrated model
The models which take bus progression into consideration, are able to offer operational benefits to bus vehicles on the target arterial, evidenced by reduction in the average bus delay.
Model-2 may yield a slight reduction in bus delay. This is due to that Model-2 has ignored the stochastic nature of bus dwell time at bus stops.
Model-2 and 4 outperform Model-1, and Model-5 outperforms both Model-2 and Model-4

## Slide 41: Case Study
Loading factor on buses | Passenger ratio k
12 | 0.8
18 | 1.2
30 | 2
7.5 | 0.5
It can be expected that the integrated model should be only applied when the difference between numbers passengers on two types of vehicles is small
When the number of passengers on buses dominates that on passenger cars, bus progression model may be preferred, and vice versa.
The system performance is quite sensitivity to the preference factor k

## Slide 42: Case Study
Chart: AVG BUS DELAY (SEC)
| 0.5 | 0.8 | 1.2 | 2
 | 131.3 | 126.25 | 127.6667 | 128.3
Chart: AVG PASSENGER CAR DELAY (SEC)
| 0.5 | 0.8 | 1.2 | 2
 | 138.3 | 124.366 | 113.9667 | 124.9
Chart: AVG PER PERSON DELAY (SEC)
| 0.5 | 0.8 | 1.2 | 2
 | 135.9667 | 125.2033 | 121.4394 | 127.1667
Chart: AVG NUMBER OF STOPS
| 0.5 | 0.8 | 1.2 | 2
 | 2.1 | 2.06 | 2.07 | 2.1033
Model-5, an integrated progression model that accounts for both buses and passenger cars, performs better when the ratio between passengers on the two types of vehicles is close to 1, as expected.
This may be because the constraints in the integrated guarantee both bus bands and passenger car bands which is unnecessary and may limit the bandwidth for the type of vehicle with significantly higher volume.

## Slide 43: Outline
Literature Review
Problem Nature and Modelling Framework
Methodology
Case Study
Conclusions and Future Study

## Slide 44: Conclusions
Due to the limited functions of the active transit signal priority control and the strengths of arterial signal progression, this study has developed a bus progression system to facilitate bus movements on an arterial.
The key features of the developed model include:
  1) the impact of bus dwell time at a bus stop between intersections on the progression design;
  2) the stochastic nature of bus dwell time;
  3) the capacity of bus stops; and
  4) the competition on the green band between buses and passenger cars
The simulation results demonstrate that the proposed model can reduce both bus passenger delays and average person delays for vehicles in the entire network, compared to the conventional progression models.

## Slide 45: Future Research
Developing a set of rigorous criteria that can compute the trade-off between bus based and passenger-car-based progression models and select the proper one in real time based on the detected traffic conditions
An extensive sensitivity analysis with field data and simulation experiments

## Slide 46: Thank you
Questions and Comments

## Slide 47: Methodology
How to determine ?
Probability of buses being in a band is
  Where, is bus arrival rate and is bandwidth of band
The probability that the number of buses in a band does not exceed the capacity should be greater than a predetermined , which can be expressed as,
  Where, is the bus stop capacity
Then can be determined by
A deterministic model

## Slide 48
An evaluation module
How to determine ?
1) set a minimum band and
2)
3)
4)
5) the number of different values of is
A band smaller than that is meaningless operationally.
Based on the bandwidth resolution of 1 second
The smaller one among and the green time
upper bound
lower bound
Minimum interval
Methodology