## Slide 1: An Integrated Traffic Control System for Urban Freeway Corridors under Non-recurrent Congestion

## Slide 2: Non-recurrent Congestion & Potential Solutions
A Urban Freeway Corridor System
Non-recurrent Congestion
Undermine capacity
Decrease efficiency
Up to 60% freeway delay (Zhang, 1997)
Potential Solutions I – Detour Operations
Utilize available parallel arterial capacity
Relieve freeway congestion
Potential Solutions II – Ramp Metering
Control the access to freeway mainline
High speeds and throughput on freeway
Potential Solutions III – Arterial Signal Optimization
Reduce stops, delays, and queuing
Improve Level of Service at Intersections

## Slide 3: New Problems Arising !
B. Off-ramp Congestion
A. On-ramp Spillback
C. Arterial Spillback and Blockages
A shift of congestion between arterials and freeways
Even worse traffic conditions than the incident impact
Integrated control strategies need to be developed

## Slide 4: Outline
Critical issues in developing an integrated traffic control system for non-recurrent congestion management
Findings of Literature Review
Primary Research Tasks and Modelling Framework
Model Development
Summary and Future Research

## Slide 5: Outline
Critical issues in developing an integrated traffic control system for non-recurrent congestion management
Findings of Literature Review
Primary Research Tasks and Modelling Framework
Model Development
Summary and Future Research

## Slide 6: Critical Issues of the Integrated Control
I – How to choose proper control boundaries?
V – How to update ramp metering and signal timing plans to prevent the formation of local bottlenecks?
II – How to model dynamic traffic flow evolutions along the corridor network?
III – How to capture the interaction between freeway and arterial?
IV – How to design diversion control strategies in response to time-varying traffic conditions?
VI – How to solve the optimization model efficiently for real-time operations?
I – How to choose proper control boundaries?
II – How to model dynamic traffic flow evolutions along the corridor network?
III – How to capture the interaction between freeway and arterial?
IV – How to design diversion control strategies in response to time-varying traffic conditions?
V – How to update ramp metering and signal timing plans to prevent the formation of local bottlenecks?
VI – How to solve the optimization model efficiently for real-time operations?

## Slide 7: Critical Issues of the Integrated Control
I – How to choose proper control boundaries?
V – How to update ramp metering and signal timing plans to prevent the formation of local bottlenecks?
II – How to model dynamic traffic flow evolutions along the corridor network?
III – How to capture the interaction between freeway and arterial?
IV – How to design diversion control strategies in response to time-varying traffic conditions?
VI – How to solve the optimization model efficiently for real-time operations?
Incident nature, available corridor capacity
Trade-off between freeway and arterial system

## Slide 8: Critical Issues of the Integrated Control
I – How to choose proper control boundaries?
V – How to update ramp metering and signal timing plans to prevent the formation of local bottlenecks?
II – How to model dynamic traffic flow evolutions along the corridor network?
III – How to capture the interaction between freeway and arterial?
IV – How to design diversion control strategies in response to time-varying traffic conditions?
VI – How to solve the optimization model efficiently for real-time operations?
Interaction with Control Variables
Traffic State Prediction and Estimation (constraints)
System Performance (objective function)

## Slide 9: Critical Issues of the Integrated Control
I – How to choose proper control boundaries?
V – How to update ramp metering and signal timing plans to prevent the formation of local bottlenecks?
II – How to model dynamic traffic flow evolutions along the corridor network?
III – How to capture the interaction between freeway and arterial?
IV – How to design diversion control strategies in response to time-varying traffic conditions?
VI – How to solve the optimization model efficiently for real-time operations?
Flow exchange at on-ramps and off-ramps
Project the time-varying impact of detoured traffic on existing traffic patterns

## Slide 10: Critical Issues of the Integrated Control
I – How to choose proper control boundaries?
V – How to update ramp metering and signal timing plans to prevent the formation of local bottlenecks?
II – How to model dynamic traffic flow evolutions along the corridor network?
III – How to capture the interaction between freeway and arterial?
IV – How to design diversion control strategies in response to time-varying traffic conditions?
VI – How to solve the optimization model efficiently for real-time operations?

## Slide 11: Critical Issues of the Integrated Control
I – How to choose proper control boundaries?
V – How to update ramp metering and signal timing plans to prevent the formation of local bottlenecks?
II – How to model dynamic traffic flow evolutions along the corridor network?
III – How to capture the interaction between freeway and arterial?
IV – How to design diversion control strategies in response to time-varying traffic conditions?
VI – How to solve the optimization model efficiently for real-time operations?

## Slide 12: Outline
Critical issues in developing an integrated traffic control system for non-recurrent congestion management
Findings of Literature Review
Primary Research Tasks and Modelling Framework
Model Development
Summary and Future Research

## Slide 13: Findings of Literature Review
Limited research has been done regarding determining the control boundaries for integrated corridor control
Simplified network flow formulations
Lack of consideration on local bottlenecks during severe congestion (e.g. turning bay spillback and blockages)
Queue arrival and departure with respect to different types of intersection lane channelization
Intersection signal timing – oversimplified, multiple phases, synchronization
Flow exchanges at on-off ramps
The dynamic impact of detoured traffic on existing demand patterns
Interactions between the freeway and arterial
The multi-objective nature of the integrated control has not been fully addressed

## Slide 14: Outline
Critical issues in developing an integrated traffic control system for non-recurrent congestion management
Findings of Literature Review
Primary Research Tasks and Modelling Framework
Model Development
Summary and Future Research

## Slide 15: Primary Research Tasks and Modeling Framework
Base Model: Single Segment Corridor Control
Enhanced Signal Timing Optimization
Modeling Framework
Solution Algorithms
Extended Model: Multi-segment Corridor Control
Network Flow Formulations
Enhanced Network Formulations Accounting for Local Bottlenecks
A Successive Optimization Framework
Part II - Integrated Control Strategies
Part I - Arterial Signal Optimization
considering Spillback and Lane Blockage
Part III - Model Solution and Real-time Application

## Slide 16: Outline
Critical issues in developing an integrated traffic control system for non-recurrent congestion management
Findings of Literature Review
Primary Research Tasks and Modelling Framework
Model Development
Summary and Future Research

## Slide 17: Part I - An Enhanced Arterial Signal Optimization Model
Task 1
An Arterial Network Flow Model to account for Local Bottlenecks (Spillback and Lane Blockage)
Task 2
Traffic Signal Timing Enhancement for Local Bottleneck Management

## Slide 18: Task 1: Arterial Network Flow Formulations
  Departure flows
  Link-based queue
  Arrival flows
Basic Concept
A link-based model
?
Discrete Time Steps
Dynamic State Equations
Queue Evolution
Limitation: Not compatible with multiple phase

## Slide 19: Task 1: Arterial Network Flow Formulations
Limitation: Inaccurate modeling of traffic flow discharge process at shared lanes
A movement-based model
  Departure flows
  Movement-based queues
  Arrival flows
?
  Shared Lane Problem

## Slide 20: Task 1: Arterial Network Flow Formulations
Is it possible to use a single formulation to address all above issues?

## Slide 21: Task 1: Arterial Network Flow Formulations
The proposed solution:
A lane-group-based model
I
II
III
  Departure flows
  Arrival flows
  2 lane groups
  Departure flows
  3 lane groups
  Arrival flows
  Departure flows
  1 lane group
  Arrival flows
  Integrate the link-based model and movement-based model into a single formulation
  Capture the evolution of physical queues with respect to the signal status, arrivals, and departures
  Provide better accuracy for modeling arrival and departure process at shared approach lanes
Key Features

## Slide 22: Task 1: Arterial Network Flow Formulations
Demand Origins
Upstream Arrivals
Model Development
Approach the End of Queue
Merge into Lane Groups
Departure
Flow Conservation

## Slide 23: Task 1: Arterial Network Flow Formulations
Key Formulations
Demand Origins
Upstream Arrivals
Approach the End of Queue
Merge into Lane Groups
Departure Process
Flow Conservation

## Slide 24: Task 1: Arterial Network Flow Formulations
Demand Origins
Flow rate entering downstream link i from demand entry r
Demand flow rate at entry r
Existing queued vehicles ( in the unit of veh/h) at entry r
Discharge capacity of link i
Available space of link i (in the unit of veh/h)

## Slide 25: Task 1: Arterial Network Flow Formulations
Demand Origins
Queue waiting at entry r at step k+1 (vehs)
Queue waiting at entry r at step k (vehs)
Demand flow rate at entry r at step k
(veh/h)
Flow rate entering downstream link i from demand entry r
(veh/h)

## Slide 26: Task 1: Arterial Network Flow Formulations
Key Formulations
Demand Origins
Upstream Arrivals
Approach the End of Queue
Merge into Lane Groups
Departure Process
Flow Conservation

## Slide 27: Task 1: Arterial Network Flow Formulations
Upstream Arrivals
For Internal Links
Upstream inflow of link i at step k (vehs)
Set of upstream links of link i
Flow actually depart from link j to link i at step k (vehs)

## Slide 28: Task 1: Arterial Network Flow Formulations
Upstream Arrivals
For source Links
Upstream inflow of link i at step k (vehs)
Flow rate entering downstream link i from demand entry r at step k (veh/h)

## Slide 29: Task 1: Arterial Network Flow Formulations
Key Formulations
Demand Origins
Upstream Arrivals
Approach the End of Queue
Merge into Lane Groups
Departure Process
Flow Conservation

## Slide 30: Task 1: Arterial Network Flow Formulations
Approach the End of Queue
Approaching speed from upstream to the end of queue at link i at step k
Free-flow speed of link i
Density from upstream to the end of queue at link i at step k
Minimum density
Jam density
Minimum speed

## Slide 31: Task 1: Arterial Network Flow Formulations
Approach the End of Queue
Density from upstream to the end of queue at link i at step k (veh/mile/lane)
Number of vehicles at link i at step k
Total number of vehicles in queue of link i at step k
Length of link i
Number of lanes of link i

## Slide 32: Task 1: Arterial Network Flow Formulations
Approach the End of Queue
Flows arriving at the end of queue of link i at step k (vehs)
Flows potentially arriving at the end of queue at step k (vehs)
Maximum number of vehicles that can arrive at the end of queue at step k (vehs)

## Slide 33: Task 1: Arterial Network Flow Formulations
Key Formulations
Demand Origins
Upstream Arrivals
Approach the End of Queue
Merge into Lane Groups
Departure Process
Flow Conservation

## Slide 34: Task 1: Arterial Network Flow Formulations
Merge into Lane Groups
Flows joining lane group m of link i at step k (vehs)
Set of downstream links of link i
Flows arriving at the end of queue of link i at step k (vehs)
Turning proportion from link i to j
Binary variable indicating whether movement from link i to j uses lane group m

## Slide 35: Task 1: Arterial Network Flow Formulations
Key Formulations
Demand Origins
Upstream Arrivals
Approach the End of Queue
Merge into Lane Groups
Departure Process
Flow Conservation

## Slide 36: Task 1: Arterial Network Flow Formulations
Departure Process
Flows potentially depart from link i to j at step k (vehs)
Queues of lane group m of link i at step k (vehs)
Discharging capacity of lane group m at link i (vehs)
Binary value indicating whether signal phase p of intersection n is set to green at step k
Percentage of traffic in lane group m going from link i to j
Flows joining the queue of lane group m of link i at step k (vehs)

## Slide 37: Task 1: Arterial Network Flow Formulations
Departure Process
Binary variable indicating whether movement from link i to j uses lane group m
Turning proportion from link i to j at step k
Percentage of traffic in lane group m going from link i to j

## Slide 38: Task 1: Arterial Network Flow Formulations
Departure Process
Flows potentially depart from link i to j at step k (vehs)
Available downstream capacity allocated for flows from link i
Flows actually depart from link i to j at step k (vehs)

## Slide 39: Task 1: Arterial Network Flow Formulations
Departure Process
Flows actually depart from link i to j at step k (vehs)
Binary variable indicating whether movement from link i to j uses lane group m
Flows actually depart from lane group m of link i at step k (vehs)

## Slide 40: Task 1: Arterial Network Flow Formulations
Key Formulations
Demand Origins
Upstream Arrivals
Approach the End of Queue
Merge into Lane Groups
Departure Process
Flow Conservation

## Slide 41: Task 1: Arterial Network Flow Formulations
Flow Conservation
Queues of lane group m of link i at step k+1 (vehs)
Queues of lane group m of link i at step k (vehs)
Flows joining the queue of lane group m of link i at step k (vehs)
Flows actually depart from lane group m of link i at step k (vehs)

## Slide 42: Task 1: Arterial Network Flow Formulations
Flow Conservation
Total number of vehicles queued at link i at step k+1 (vehs)
Queues of lane group m of link i at step k+1 (vehs)

## Slide 43: Task 1: Arterial Network Flow Formulations
Flow Conservation
Total number of vehicles at link i at step k+1 (vehs)
Total number of vehicles at link i at step k (vehs)
Flows actually depart from upstream to link i at step k (vehs)
Flows actually depart from link i to downstream at step k (vehs)

## Slide 44: Task 1: Arterial Network Flow Formulations
Flow Conservation
Available space of link i at step k+1 (vehs)
Storage space of link i (vehs)
Total number of vehicles at link i at step k+1 (vehs)

## Slide 45: Capturing Local Bottlenecks
Why?
    The storage capacity of the intersection approach lane
    Lane group queue interaction
Further Enhancement
to account for queue interaction
Right-through lane group
Left turn lane group
Blockage

## Slide 46: Capturing Local Bottlenecks
Spillback
Partial
Blockage
Complete
Blockage
Spillback
Propose the concept of “Blocking Matrix” to model the dynamic interaction between various lane group queues

## Slide 47: Capturing Local Bottlenecks
Spillback
Partial
Blockage
Complete
Blockage
Spillback
A value between 0 and 1

## Slide 48: Capturing Local Bottlenecks
The percentage of merging capacity reduction for lane group m due to the queue spillback at lane group m’ at step k
Constant parameter related to driver’s response to lane blockage and geometry features
Approximates the fraction of merging lanes occupied by the overflowed traffic from lane group m’
Potential flows may merge into group m at link i at step k (vehs)

## Slide 49: Capturing Local Bottlenecks
Potential flows may merge into group m at link i at step k (vehs)
Number of vehicles bound to lane group m but queued outside at link i due to blockage at step k
Flows arriving at the end of queue of link i at step k (vehs)
Turning proportion from link i to j
Binary variable indicating whether movement from link i to j uses lane group m

## Slide 50: Capturing Local Bottlenecks
Key Enhancement
Demand Origins
Upstream Arrivals
Approach the End of Queue
Merge into Lane Groups
Departure Process
Flow Conservation
Enhanced Formulations

## Slide 51: Capturing Local Bottlenecks
Number of vehicles allowed to merge into group m at link i at step k (vehs)
Available storage capacity of lane group m at step k
Number of vehicles allowed to merge into group m at link i at step k considering the blockage effect (vehs)
Key Enhancement

## Slide 52: Part I - An Enhanced Arterial Signal Optimization Model
Task 1
Network Enhancement Approach to account for Local Bottlenecks (Queue Interactions and Blockages)
Task 2
Traffic Signal Timing Enhancement for Local Bottleneck Management

## Slide 53: Task 2: An Enhanced Signal Optimization Model
Task 2
Traffic Signal Timing Enhancement for Local Bottleneck Management
Control Objectives
  Minimize total travel time and queue time – under saturated conditions
  Maximize total throughput – oversaturated conditions

## Slide 54: Task 2: An Enhanced Signal Optimization Model
Task 2
Traffic Signal Timing Enhancement for Local Bottleneck Management
Experimental Design
  1. A hypothetical arterial
  2. Three traffic demand levels
  3. Comparison with TRANSYT-7F with the turning bay spillover factor set

## Slide 55: Task 2: An Enhanced Signal Optimization Model
Task 2
Traffic Signal Timing Enhancement for Local Bottleneck Management
Control Plans
  The proposed model tends to select shorter cycle length to reduce the chance of blockages
The proposed model
TRANSYT-7F

## Slide 56: Task 2: An Enhanced Signal Optimization Model
Task 2
Traffic Signal Timing Enhancement for Local Bottleneck Management
Control Performance
  1. Low- and medium demand scenario: less total delay and total queue time but less total throughput
  2. High-demand scenario: less total queue time and more total throughput

## Slide 57
Summary
The proposed model outperforms TRANSYT-7F in terms of total system queue time for all experimental demand scenarios
For oversaturated traffic conditions, in terms of the total system queue time and total system throughput, the proposed model can mitigate the congestion and blockage more effectively than TRANSYT-7F due to the use of enhanced network flow formulations.

## Slide 58: Part II – The Integrated Corridor Control Model
The Arterial Model
The Freeway Model
Interaction between freeway and arterial
Overall Corridor Model

## Slide 59: Part II – The Integrated Corridor Control Model
The Arterial Model
(done)
The Freeway Model
Interaction between freeway and arterial
Overall Corridor Model

## Slide 60: The Freeway Model
The Freeway Model
Basic Concept
METANET Model
(Messmer and Papageorgiou, 1990)
Discrete Time Steps
Dynamic State Equations
Sub-sections of freeway mainline
Extension
Sections near the off-ramp and on-ramp

## Slide 61: The Freeway Model
Sections near the off-ramp and on-ramp
Actual flow rate leaving from the freeway link right before the off-ramp at time t
Normal exit rate for off-ramp during interval h
Driver compliance rate to the detour operation
Diversion rate for off-ramp during interval h
Actual entering flow rate into off-ramp at time t
Density at time t
Speed at
time t
Number of lanes

## Slide 62: The Freeway Model
The Freeway Model
Basic Concept
METANET Model
(Messmer and Papageorgiou, 1990)
Discrete Time Steps
Dynamic State Equations
Sub-sections of freeway mainline
Extension
Sections near the off-ramp and on-ramp

## Slide 63: The Freeway Model
Sections near the off-ramp and on-ramp
Actual flow rate entering the freeway link right after the off-ramp at time t
Actual flow rate leaving from the freeway link right before the off-ramp at time t
Actual entering flow rate into off-ramp at time t

## Slide 64: The Freeway Model
The Freeway Model
Basic Concept
METANET Model
(Messmer and Papageorgiou, 1990)
Discrete Time Steps
Dynamic State Equations
Sub-sections of freeway mainline
Extension
Sections near the off-ramp and on-ramp

## Slide 65: The Freeway Model
Sections near the off-ramp and on-ramp
Actual flow rate entering the freeway link right after the on-ramp at time t
Actual flow rate leaving from the freeway link right before the on-ramp at time t
Actual merging flow rate into freeway from on-ramp at time t

## Slide 66: Part II – The Integrated Corridor Control Model
The Arterial Model
The Freeway Model
Interaction between freeway and arterial
Overall Corridor Model
A. On-off Ramps
B. The impact of detour traffic

## Slide 67: The On-ramp Model
Interaction between freeway and arterial
A. On-off Ramps (On-ramp)
Basic Concept
Model ramps as simplified arterial links with the lane-group concept
Modify departure process for on-ramp
Modify arrival process for off-ramp
Revised departure process

## Slide 68: The On-ramp Model
A. On-off Ramps (On-ramp)
Actual flow rate allowed to merge into freeway from on-ramp
Potential number of vehicles to merge into freeways (waiting+arrival)
Discharging capacity under the ramp metering
Available downstream freeway capacity (veh/h)

## Slide 69: The Off-ramp Model
Interaction between freeway and arterial
A. On-off Ramps (Off-ramp)
Basic Concept
Model ramps as simplified arterial links with the lane-group concept
Modify departure process for on-ramp
Modify arrival process for off-ramp
Revised arrival process

## Slide 70: The Off-ramp Model
A. On-off Ramps (Off-ramp)
Actual flow rate entered the off-ramp
Potential flow rate to enter the off-ramp (normal+detour)
Off-ramp capacity (veh/h)
Available space at the off-ramp (veh/h)

## Slide 71: The Impact of Detour Traffic
Interaction between freeway and arterial
B. The impact of detour traffic
Basic Concept
Integrate the “sub-flow” concept with the lane-group-based arterial model
Revised arrival process
Detour Traffic
Arterial Traffic

## Slide 72: The Impact of Detour Traffic
Interaction between freeway and arterial
B. The impact of detour traffic
Upstream Arrivals
Approach the End of Queue
Merge into Lane Groups
Departure Process
Flow Conservation
Model Extensions

## Slide 73: The Overall Corridor Model
The Arterial Model
The Freeway Model
Interaction between freeway and arterial
Overall Corridor Model
On-off Ramps
The impact of detour traffic

## Slide 74: Part II – The Integrated Corridor Control Model
Step 1
Base Model - Integrated Control of a Single Corridor Segment
Step 2
Extended Model - Integrated Control of a Multi-segment Corridor

## Slide 75: Part II – The Integrated Corridor Control Model
Step 1
Base Model - Integrated Control of a Single Corridor Segment
Expected Output:
    Diversion rates at the off-ramp
    Arterial signal timings: cycle length, offsets, and splits
    Incident upstream on-ramp metering rates

## Slide 76: Part II – The Integrated Corridor Control Model
Step 1
Base Model - Integrated Control of a Single Corridor Segment
Key Formulations
  Max. Total Corridor Throughput
  Min. Total Spent Time by Detour Traffic
Operational Constraints
Network Flow Constraints

## Slide 77: Part II – The Integrated Corridor Control Model
Operational Constraints
Cycle length constraint
Green time constraint
The sum of green times and clearance times
should be equal to cycle length.
Offset constraint
Metering rate constraint
Diversion rate constraint

## Slide 78: Part II – The Integrated Corridor Control Model
Step 1
Base Model - Integrated Control of a Single Corridor Segment
Step 2
Extended Model - Integrated Control of a Multi-segment Corridor

## Slide 79: Part II – The Integrated Corridor Control Model
Expected Output:
    Control boundaries for detour operations
    Detour plans
    Diversion rates at each off-ramp
    Arterial signal timings: cycle length, offsets, and splits
    Incident upstream on-ramp metering rates
Step 2
Extended Model - Integrated Control of a Multi-segment Corridor

## Slide 80: Part II – The Integrated Corridor Control Model
Formulations
  Additional set of decision variables for detour route choice
Step 2
Extended Model - Integrated Control of a Multi-segment Corridor
Enhanced Network Flow Constraints

## Slide 81: Part III – Solution Algorithms for Integrated Control
Module I: A compromised GA to solve the proposed bi-objective model (Gen and Cheng, 1998)
Module II: A successive optimization framework for real-time application with variable rolling time window
Ideally best point
Solution
Difficulties
    Dynamic, discrete-time and complex system
    Non-linear constraints
    Time-consuming process to obtain the Pareto solution set
    Large-scale
    Dramatic traffic pattern changes

## Slide 82: On-line Estimation of Diversion Compliance Rates
Estimation of compliance rate
Measurement of flow rate at the off-ramp
Measurement of flow rate at the freeway upstream
Normal exit rate
Applied diversion rate

## Slide 83: Case Studies – The Base Model
Experiment Design
    I-95 corridor northbound
    MD198 and MD216
    6 arterial intersections
    2 traffic demand levels
    2 levels of incident effect
    35-min control period
II. Peak hour (high demand level)
I. Off-peak hour (low traffic demand level)
II. 2 lanes blocked due to incident
I. 1 lane blocked due to incident
4 test scenarios
  Scenario 1: Off-peak with 1 lane blocked
  Scenario 2: Off-peak with 2 lanes blocked
  Scenario 3: Peak with 1 lane blocked
  Scenario 4: Peak with 2 lanes blocked
Plan C
  5-min normal operation
  20-min incident period
  10-min incident recovery

## Slide 84: Case Studies – The Base Model
Step- 1:
Evaluate the performance of the proposed model with systematically varied weights to provide operational guidelines for decision makers in best weighting importance between both control objectives under a given scenario
Step- 2:
With a set of properly selected weights from Step - 1, compare the model performance with other two strategies
Equity
Efficiency

## Slide 85: Case Studies – The Base Model
Step- 1:
Evaluate the performance of the proposed model with systematically varied weights to provide operational guidelines for decision makers in best weighting importance between both control objectives under a given scenario
Equity
Efficiency
Step- 2:
With a set of properly selected weights from Step - 1, compare the model performance with other two strategies

## Slide 86: Case Studies – The Base Model
Step- 1: Objective function values under different weight assignment (w1/w2)
  Scenario 1: Off-peak with 1 lane blocked
  Scenario 2: Off-peak with 2 lanes blocked
  Scenario 3: Peak with 1 lane blocked
  Scenario 4: Peak with 2 lanes blocked

## Slide 87: Case Studies – The Base Model
Step- 1: Travel Time (Detour Route v.s. Freeway Mainline)
Scenario 2

## Slide 88: Case Studies – The Base Model
Step- 1: Travel Time (Detour Route v.s. Freeway Mainline)
Scenario 3

## Slide 89: Case Studies – The Base Model
Step- 1: Travel Time (Detour Route v.s. Freeway Mainline)
Scenario 4

## Slide 90
Single control objective may effectively maximize the utilization of corridor capacity under light traffic and incident conditions, however it may cause unbalanced traffic conditions under over-saturated conditions which will degrade the diversion compliance rates
Traffic operators need to properly select the weighting factors between two control objectives to achieve the best operational efficiency while balancing the traffic conditions

## Slide 91: Case Studies – The Base Model
Step- 1:
Evaluate the performance of the proposed model with systematically varied weights to provide operational guidelines for decision makers in best weighting importance between both control objectives under a given scenario
Equity
Efficiency
Step- 2:
With a set of properly selected weights from Step - 1, compare the model performance with other two strategies

## Slide 92: Case Studies – The Base Model
Plan A
  No Control – base line
Plan B
  Local Responsive Control
  Detour – Static User Equilibrium (UE)
  On-ramp metering – ALINEA
  Arterial signal timing – TRANSYT-7F
Plan C
  The Proposed control model
Step- 2: Comparison with other strategies
4 test scenarios
  Scenario 1: Off-peak with 1 lane blocked
  Scenario 2: Off-peak with 2 lanes blocked
  Scenario 3: Peak with 1 lane blocked
  Scenario 4: Peak with 2 lanes blocked

## Slide 93: Case Studies – The Base Model
MOE -1. Accumulated Total Travel Time Savings
Scenario 1
w1/w2=10/0
Scenario 2
w1/w2=10/0
Scenario 3
w1/w2=6/4
Scenario 4
w1/w2=5/5

## Slide 94: Case Studies – The Base Model
MOE-2. Accumulated Total Corridor Throughput Increases
Scenario 1
w1/w2=10/0
Scenario 2
w1/w2=10/0
Scenario 3
w1/w2=6/4
Scenario 4
w1/w2=5/5
The proposed integrated control model outperforms other control strategies under all experimental scenarios

## Slide 95: Case Studies – The Extended Model
Experiment Design: A 12-mile hypothetical corridor with 12 exits and 36 arterial intersections

## Slide 96: Case Studies – The Extended Model
Step- 1:
Investigate the control area variation with respect to different weight assignment settings, and its impact on the system MOEs
Step- 2:
Compare the performance of the extended model with the base model under the same incident scenario and the same control objective

## Slide 97: Case Studies – The Extended Model
Step- 1:
Investigate the control area variation with respect to different weight assignment settings, and its impact on the system MOEs
Step- 2:
Compare the performance of the extended model with the base model under the same incident scenario and the same control objective

## Slide 98: Case Studies – The Extended Model
Step- 1: The variation of control boundaries
  w1/w2=10/0 and 9/1
  w1/w2=5/5, 4/6, and 3/7
  w1/w2=2/8 and 1/9
  w1/w2=0/10
  w1/w2=8/2, 7/3, and 6/4
Preliminary Findings:
The control boundaries shrink with the weight assignment between two control objectives varying from 10/0 to 0/10
There exists a critical control area beyond which the total corridor throughput no longer increases.
The number of incident downstream on-ramps used to divert traffic back to the freeway is less than that of incident upstream off-ramps.

## Slide 99: Case Studies – The Extended Model
Step- 1: Determine the proper control boundaries
  w1/w2=10/0
  w1/w2=8/2
  Total corridor throughput decreases only 3.2%
  Total spent time by detour traffic decreases 19.8%

## Slide 100: Case Studies – The Extended Model
Step- 1: Distribution of diversion flows
  w1/w2=10/0 and 9/1
  w1/w2=8/2, 7/3, 6/4
The diversion flows are not evenly distributed over the upstream off-ramps. An off-ramp closer to the incident location has carried more diversion flows
The most upstream off-ramps only carry a small percent of diversion traffic but significantly increase the total time spent

## Slide 101: Case Studies – The Extended Model
Step- 1:
Investigate the control area variation with respect to different weight assignment settings, and its impact on the system MOEs
Step- 2:
Compare the performance of the extended model with the base model under the same incident scenario and the same control objective

## Slide 102: Case Studies – The Extended Model
Step- 2: Comparison with the base model under the same incident scenario and the same control objective
  The control boundaries of the base model
  Model 1
  The control boundaries of the extended model
  Model 2
  The same control objective: Maximizing the total corridor throughput
The extended model outperforms the base model in terms of the total corridor throughput
The extended model can also significantly decrease the average total queue time on detour links and at the side street links

## Slide 103: Outline
Critical issues in developing an integrated traffic control system for non-recurrent congestion management
Findings of Literature Review
Primary Research Tasks and Modelling Framework
Model Development
Summary and Future Research

## Slide 104: Summary of Contributions
Develop an effective operational framework to integrate different control strategies for incident management
Base Model: Single Segment Corridor Control
Enhanced Signal Timing Optimization
Extended Model: Multi-segment Corridor Control
Network Flow Formulations
Enhanced Network Formulations Accounting for Local Bottlenecks
Integrated Level
Local Level

## Slide 105: Summary of Contributions
Develop an enhanced arterial signal optimization model to produce control strategies that can effectively prevent the formation of local bottlenecks

## Slide 106: Summary of Contributions
Construct an overall corridor model that can capture network flow evolution in a dynamic control environment
The Overall Corridor Model

## Slide 107: Summary of Contributions
Formulate a set of mathematical models solved by an efficient algorithm for design of integrated corridor control strategies in real time
A Multi-objective Framework
Base Model
Extended Model
  Substantially improved operational performance with balanced traffic conditions between the freeway and detour routes
  Less negative impact on the local arterial and better system performance compared with the base model
GA-based Heuristic
+
A successive optimization framework

## Slide 108: Future Research
Development of robust solution algorithms for the proposed models when available control inputs are missing or contain some errors
Development of efficient solution algorithms for large-scale network-wide control
Development of an intelligent interface with advanced surveillance systems

## Slide 109: Thanks for your attention! Q & C?

## Slide 110: Computational Performance
Projection Stage
Update Interval
Convergence Failure
The Base Model
The Extended Model
4-min
10-min
1 cycle length
2 cycle length
<3%
<10%

## Slide 111: System Application
Intelligent On-line Traffic Management System
    Assist transportation agencies to deal with recurrent or non-recurrent congestion
    Improve the operational efficiency for the urban traffic corridor system